## Slide 1: Vulture mine tailings
Nicolas Boon
Audrey Lang
Nicole Stanczak

## Slide 2: Site background
Wickenburg, Arizona
Gold mine
  1863- Operation began
  1942- Mine closed
Mined by open-cut methods
  Treatment: Cyanide leaching
Tailing migration
  Cloudbursts
  Entered into a wash south of the mine
Audrey Lang
Figure 1: Wash south of Vulture Mine

## Slide 3: Client, Tech advisor, stakeholders
Client
  Bureau of Land Management (BLM)
  Mr. Matt Plis
  Dr. Bill Harris, PhD, PE
Technical Advisor
  Dr. Bridget Bero
Stakeholders
  BLM
  United States and Arizona Citizens
[1]
Nicole Stanczak

## Slide 4: Project overview
Examine and assess the risks that accompany the migration of mine tailings
Produce a Preliminary Assessment/Site Inspection (PA/SI) following the CERCLA process
Use results to determine if the BLM should proceed with further CERCLA actions
Audrey Lang

## Slide 5: Work Plan
Details protocols to be followed when collecting samples
Contains Health & Safety Plan and Sampling & Analysis Plan
  Health & Safety Plan provides:
    Emergency contact information
    Personal Protection Equipment
    Details of chemicals being used
    Descriptions of potential field encounters
Nicolas Boon
Figure 2: Snake encounter

## Slide 6: Sampling plan
Created maps and identified the range of the site
Created a grid on the map to identify potential sampling spots
Soil Samples
  160 Grid based soil samples
  8 Background samples
  32 Samples between Hot Spots and Random Spots
Nicole Stanczak

## Slide 7: Location of Vulture mine
[2]
Nicole Stanczak

## Slide 8: Field Sampling
75 Grid soil samples
4 Background samples
25 Hot spot samples
Figure 3: Grid soil sample collection
Figure 5: Grid soil sample collection
Figure 4: Hot spot soil sample
Nicole Stanczak

## Slide 9: Sampling locations on the wash
[3]
Nicole Stanczak

## Slide 10: Gridded Section of the wash
[4]
Nicole Stanczak

## Slide 11: XRF Screening
Divide each bag into 9 sections
Drop the highest and lowest reading and take the average of the 7 readings
20% of samples sent to Environmental Analysis Laboratory
Audrey Lang
Figure 6: Nicole XRF screening
Figure 7: Soil sample
Figure 8: Audrey XRF screening

## Slide 12: Metal Extractions
5g of each soil sample
Nitric Acid and 30% Hydrogen Peroxide
Cesium Sulfide and Lanthanum Sulfide
Figure 10: Nick weighing out samples
Figure 11: Drying soil samples
Audrey Lang

## Slide 13: Total Metals Testing
Sample preparation
Microwave Digest
Figure 13: Holding cells
Figure 12: Addition of Nitric Acid to sample
Audrey Lang

## Slide 14: Concentration Mapping of Lead
[6]
Below Residential Remediation Level (0-399 mg/kg)
Below Non-Residential Remediation Level (400-799 mg/kg)
Higher Than Non-Residential Remediation Level (800+ mg/kg)
Nicolas Boon

## Slide 15: Concentration Mapping of Lead
[6]
[7]
Below Residential Remediation Level (0-399 mg/kg)
Below Non-Residential Remediation Level (400-799 mg/kg)
Higher Than Non-Residential Remediation Level (800+ mg/kg)
Nicolas Boon

## Slide 16: Concentration Mapping of Lead
[6]
[8]
Below Residential Remediation Level (0-399 mg/kg)
Below Non-Residential Remediation Level (400-799 mg/kg)
Higher Than Non-Residential Remediation Level (800+ mg/kg)
Nicolas Boon

## Slide 17: Concentration Mapping of Lead
[6]
[9]
Below Residential Remediation Level (0-399 mg/kg)
Below Non-Residential Remediation Level (400-799 mg/kg)
Higher Than Non-Residential Remediation Level (800+ mg/kg)
Nicolas Boon

## Slide 18: Data Correlations
Lead Correlation with XRF and FAAS Results
Copper Correlation with XRF and FAAS Results
Figure 15: Lead Correlation
Figure 16: Copper Correlation
Nicolas Boon

## Slide 19: Soil Remediation levels
Nicole Stanczak

## Slide 20: Risk Assessment Scenarios
Two human risk scenarios
  Site worker
  Recreational user
Adult Lead Model
  Average concentration of lead = 1152 ppm
  90% max concentration of lead = 4277 ppm
Audrey Lang

## Slide 21: Average lead concentration
Calculations of Blood Level Concentrations: Adult Worker |  | 
Cases | Units | GSDi and PbBo from Analysis of NHANES lll
Target PbB level of concern | ug/dL | 10
PbB of adult worker, geometric mean | ug/dL | 4.8
95th percentile PbB among fetuses of adult workers | ug/dL | 14.6
Probability of fetal PbB > adult PbB | % | 12.9
Calculations of Blood Level Concentrations: Adult Recreational User |  | 
Cases | Units | GSDi and PbBo from Analysis of NHANES lll
Target PbB level of concern | ug/dL | 10
PbB of adult recreational user, geometric mean | ug/dL | 1.7
95th percentile PbB among fetuses of adult recreational user | ug/dL | 5.2
Probability of fetal PbB > adult PbB | % | 0.6
Audrey Lang

## Slide 22: 90% Max lead concentration
Calculations of Blood Level Concentrations: Adult Worker |  | 
Cases | Units | GSDi and PbBo from Analysis of NHANES lll
Target PbB level of concern | ug/dL | 10
PbB of adult worker, geometric mean | ug/dL | 13.7
95th percentile PbB among fetuses of adult workers | ug/dL | 41.9
Probability of fetal PbB > adult PbB | % | 61.2
Calculations of Blood Level Concentrations: Adult Recreational User |  | 
Cases | Units | GSDi and PbBo from Analysis of NHANES lll
Target PbB level of concern | ug/dL | 10
PbB of adult recreational user, geometric mean | ug/dL | 2.2
95th percentile PbB among fetuses of adult recreational user | ug/dL | 6.7
Probability of fetal PbB > adult PbB | % | 1.5
Audrey Lang

## Slide 23: Ecological Risk Assessment
EPA Integrated Risk Information System (IRIS)
IRIS conducted studies on rats exposed to high concentrations of lead
These rats showed distinct characteristics such as the formation of tumors
Mammals and reptiles at the site are potentially at risk if these high level of lead are ingested
Figure 17: Snake found on site
Nicole Stanczak

## Slide 24: Broader impacts
Environmental/Health
  Hikers
  Bikers
  Wildlife and endangered species
Political
  Controversial issues regarding cleanup of sites
Global
  Example for other mining sites
Nicole Stanczak

## Slide 25: Total Hours & personal costs
Personnel Cost |  | 
Position | Hours | Cost
Senior Engineer | 72 | $7,200
Environmental Engineer | 157 | $8,263
Lab Technician | 120 | $3,590
External Help | 72 | $1,900
Total | 421 | $20,953
Site Visit Expenses |  | 
Item | Rate | Cost
Transportation | $0.56/mile | $202
Hotel | $90/room | $270
Food | $8/meal | $160
Total |  | $632
Total Cost of Project |  | 
$21,914 |  | 
Audrey Lang

## Slide 26: Laboratory costs
Laboratory Costs for Metal Extractions |  |  | 
Metal Extractions | $/Sample | # of Samples | Cost
Synthetic Leaching | 4 | 28 | $112
Microwave Digest | 8 | 33 | $248
Total |  |  | $360
Laboratory Costs for FAA Testing |  |  | 
FAA Testing | $/Sample | # of Samples | Cost
Synthetic Leaching | 16 | 28 | $448
Microwave Digest | 16 | 33 | $512
Total |  |  | $960
Student Discount |  | 
Discount | M.E.+FAA Cost | Total
75% | $1,319 | $330
Audrey Lang

## Slide 27: Conclusion
Correlations validate high concentrations of lead found at the site
Recommend BLM to take further action
  Pursue a Potentially Responsible Party (PRP)
  Remedial Action
Figure 18: Mine tailing pile
Audrey Lang

## Slide 28: Acknowledgements
Thank you for all the help and support!
NAU
  Dr. Bridget Bero
  Jeff Propster
  Gary Slim
  Alina-Maria Davidescu
Sincerely,
Gold Member Inc.
BLM
  Mr. Matt Plis
  Dr. Bill Harris
  Jason Frels
  Eric Zielske

## Slide 29: References
[1] Kuer. 2013. By Nicole Nixon
[2] Google Earth: Wash Outline Samples. The Vulture Mine- Wickenburg, AZ. Available: [https://www.google.com/earth/]
[3] Google Earth: location of soil samples taken. The Vulture Mine- Wickenburg, AZ. Available: [https://www.google.com/earth/]
[4] Google Earth: Gridded north section of wash. The Vulture Mine- Wickenburg, AZ. Available: [https://www.google.com/earth/]
[5] Google Earth: Location of soil samples taken. The Vulture Mine- Wickenburg, AZ. Available: [https://www.google.com/earth/]
[6] Google Earth: south section of wash. The The Vulture Mine- Wickenburg, AZ. Available: [https://www.google.com/earth/]
[7] Google Earth: central section of wash. The Vulture Mine- Wickenburg, AZ. Available: [https://www.google.com/earth/]
[8] Google Earth: north section of wash. The Vulture Mine- Wickenburg, AZ. Available: [https://www.google.com/earth/]

## Slide 30: Questions???