## Slide 1: BASKETBALL COURT DESIGN
Team Members:
Adel Alnasser
Daij Alfahad
Hamad Alqalaf

## Slide 2: Overview
Project Understanding
Project List of Tasks
Task Testing and Analysis
Project Costs
Final Design

## Slide 3: Stakeholders, Client and Technical Advisor
Client: Dr. Edward Smaglik
Technical Advisor: Mr. Mark Lamer
Stakeholder:
Homeowner Association Management Company
http://www.research.nau.edu/newsletter/spring2011/aztrans.aspx
http://nau.edu/CEFNS/Engineering/CivilEnvironmental/Directory/Lamer/
http://www.hoamco.com/

## Slide 4: Project Description
Designing a full basketball court with maintaining the existing drainage system.
Location: Ponderosa trails unit eight.
Area of the empty land is:
0.57 Acres
Taken from Google Maps

## Slide 5: Current Conditions
The land is located by interstate I-17
Existing sub-basin approximately 1/3 of the total area
Two barrel circular culverts
Trees on the way of the proposed design
Sided by houses
No parking spots
Taken by Daij
https://gismaps.coconino.az.gov/ParcelViewer/

## Slide 6: Purpose of The Project
Developing the site.
Make use of the empty land to become a basketball court.
Meeting the residents’ satisfaction and the community.
http://www.miamitownship.com/182/Basketball-Hoop-Policy

## Slide 7: Project List of Tasks
Task 1: Project Management
Task 2: Data Collection
Task 3: Surveying
Task 4: Drainage
Task 5: Additional Features
Task 6: Final Design

## Slide 8: Data Collection
  Policies, regulations and information research.
    Ponderosa Trails Unit Eight Construction Plans and Drainage Report done by Woodson Engineering and Surveying, Inc.
    Flagstaff City Code, Title 10 and 13, Flagstaff Zoning Code and Engineering Design Standards and Specifications for New Infrastructure.
    Detention Basin Requirements - City Of Flagstaff Stormwater Design Manual (Ch.8)
    Low Impact Development - Guidance Manual for Site Design and Implementation
    Maricopa Association of Governments

## Slide 9: Surveying
Total station and data collector were used to shoot 276 points.
Auto level and measuring tape were used to determine the existing culvert dimensions, elevation and slope.
Parameters | Culvert 1 | Culvert 2
Diameter (ft) | 3 | 3
Length (ft) | 80.65 | 80.65
Slope (ft/ft) | 0.0005 | 0.0006
Points Layout from AutoCAD

## Slide 10: Topographic map
The surveying points were used to create the map.
Determining the trees’ location.

## Slide 11: Drainage (Hydrology)
NOAA Atlas 14 Data:
Precipitation Frequency (in/hr) |  |  | 
by duration | 2 years | 10 years | 100 years
5-min: | 3.54 | 5.78 | 9.77
10-min: | 2.69 | 4.4 | 7.44
15-min: | 2.23 | 3.64 | 6.15
30-min: | 1.5 | 2.45 | 4.14
60-min: | 0.93 | 1.51 | 2.56
2-hr: | 0.53 | 0.83 | 1.39
3-hr: | 0.38 | 0.58 | 0.95
6-hr: | 0.23 | 0.33 | 0.51
12-hr: | 0.14 | 0.2 | 0.29
24-hr: | 0.1 | 0.14 | 0.21

## Slide 12: Drainage (Hydrology)
Rational Equation
Q = C I A
Where:
Q is Discharge (cfs)
C is Runoff Coefficient
I is Intensity (in/hr)
A is Area (Acres)
-bar =
Sheet Flow Equation
  T =
  Where:
  T is Sheet Flow Travel Time (hr)
  n is Manning’s Roughness Coefficient
  L is Flow Length (ft)
  P is Year 24 hours Precipitation (in)
  S is Slope (ft/ft)

## Slide 13: Drainage (Hydrology)
Pre-Development |  |  |  |  | 
 | Pervious | Impervious |  |  | 
Area (Acre) | 0.570 | 0.000 |  | Total Area = | 0.570
C | 0.5 | 0.95 |  | C-bar = | 0.500
Tc (min) | 5 | 5 |  |  | 
2 years | Area (Acre) | Tc (min) | Intensity in/hr | C | Q (Cfs)
Total A | 0.570 | 5 | 3.540 | 0.500 | 1.0089
10 years | Area (Acre) | Tc (min) | Intensity in/hr | C | Q (Cfs)
Total A | 0.570 | 5 | 5.78 | 0.500 | 1.6473
100 years | Area (Acre) | Tc (min) | Intensity in/hr | C | Q (Cfs)
Total A | 0.570 | 5 | 9.77 | 0.500 | 2.78445
Post-Development |  |  |  |  | 
 | Pervious | Impervious |  |  | 
Area (Acre) | 0.490 | 0.080 |  | Total Area = | 0.570
C | 0.5 | 0.95 |  | C-bar = | 0.563
Tc (min) | 5 | 5 |  |  | 
2 years | Area (Acre) | Tc (min) | Intensity in/hr | C | Q (Cfs)
Total A | 0.570 | 5 | 3.540 | 0.563 | 1.13634
10 years | Area (Acre) | Tc (min) | Intensity in/hr | C | Q (Cfs)
Total A | 0.570 | 5 | 5.78 | 0.563 | 1.85538
100 years | Area (Acre) | Tc (min) | Intensity in/hr | C | Q (Cfs)
Total A | 0.570 | 5 | 9.77 | 0.563 | 3.13617
ΔQmax= 0.35 cfs

## Slide 14: Drainage (Hydrology)
Storage Volume “Acre-ft” | Storage Volume “ft3”
0.012 | 506

## Slide 15: Hydraulics
Existing Culverts Analysis: Based on the Pre-development discharge data and culvert dimensions.
The Peak Discharge Year | Hydrologic Element | Discharge Peak (Cfs) | Volume (ac-ft) | Area (mi2)
10-Year | Sub-Basin 15a | 9.5895 | 2.2996 | 0.180
25-Year | Sub-Basin 15a | 29.857 | 4.7718 | 0.180
100-Year | Sub-Basin 15a | 67.468 | 8.7316 | 0.180
Maximum Capacity Q= 73.6 cfs
Woodson Engineering Drainage Report

## Slide 16: Hydraulics
Required slope: 3:1
Required Freeboard: 0.5 ft
Maximum unprotected depth: 3 ft
Basin Design Dimensions Including Freeboard | 
r1 (ft) | 13.31
r2 (ft) | 5.81
H (ft) | 2.5
V (ft3) | 754.62
Water Level |  | 
Storm Event (years) | Volume (ft3) | Water level (ft)
2 | 183.28 | 1.05
10 | 296.20 | 1.45
100 | 506.00 | 2.00
Detention Basin Design

## Slide 17: Hydraulics
Side Slope =3:1

## Slide 18: Hydraulics
Basin Outlet Structure Design
Orifice Area:
Ao : Orifice area, ft2
qpb : Pre-development peak runoff, cfs
Es : water elevation in basin, ft
Eo : Elevation of bottom of orifice opening, ft
Storm Event (Years) | Ao (ft2)
2 | 0.25
10 | 0.35
100 | 0.26

## Slide 19: Hydraulics
Outlet wall structure

## Slide 20: Additional Features
Resource Protection:
  The calculation of the trees drip line to avoid any root damage.
  Diameter at Breast Height (DBH) was measured to determine the canopy area.
  Based on the resource protection calculations:
    4 trees need to be cut.
Flagstaff Zoning Code, Title 10

## Slide 21: Additional Features
Court Dimensions:
  There will be additional 2 ft on both the length and the width of the court.
  Minimum slope corner to corner= 0.8 percent.
  The concrete that will be used for the court is the same as the sidewalk structure.

## Slide 22: Additional Features
Sidewalk: According to City of Flagstaff and Maricopa Association of Governments (MAG):
Width= 5 ft
Thickness= 4 in
Slope= 1.5%
Radius at Edges= 0.25 in
Class A Portland cement concrete containing 5 to 7 percent air entrainment.
According to (MAG) detail 230, the construction joints score mark is 1/2 inch minimum depth every 5 ft.
According to (MAG) section 340 the expansion joints extent through the concrete and 1 inch through the subgrade.

## Slide 23: Additional Features
The Project meets the standards for accessible design (ADA)
Low Impact Development is not required.
Bench area will have two 8 ft long benches on one side of the court.
  The Pavement Area= 20ftx3ft= 60 ft2
Traffic Analysis:
  Installing “No parking” signage
http://commons.wikimedia.org/wiki/File:Singapore_Road_Signs_-_Restrictive_Sign_-_No_Parking.svg

## Slide 24: Costs Analysis
Total Cost of Engineering Services and Implementation | 
Engineering Services | $ 28680
Implementation | $ 13250.55
Total Cost | $ 41930.55

## Slide 25: Final Design

## Slide 26
Questions ?