## Slide 1: Copper Age Mine: Preliminary Assessment and Site Inspection
Northern Arizona Consulting
UGRADS: April 27, 2018
Laura Garcia
Spencer Harvey
Carl Haskie
Sarah Reddinger
Notes: spencer

## Slide 2: Project Background
Client: Bureau of Land Management
Location: Northwestern Arizona,
approximately 15 miles north of Kingman
Current Status: “Past Producer” [1]
Shipped mining commodities: 1900s-1940s
Objective: Perform a combined Preliminary Assessment and Site Inspection (PA/SI) via
the Comprehensive Environmental Response, Compensation, and Liability Act (CERCLA)
Figure 1: Copper Age Mine statewide location with respect to Kingman, AZ [2]
Notes: spencer
Superfund = CERCLA
BLM wants site analyzed because recreationalists and potential wildlife exposure
Identify contaminants of concern; they need to know if there is contamination and if it’s severe enough to require removal
Operational from early to mid-1900s
Past producer indicates it produced zinc, gold, and copper

## Slide 3: Project Background
Client: Bureau of Land Management
Location: Northwestern Arizona, approximately 15 miles north of Kingman
Current Status: “Past Producer” [1]
Shipped mining commodities: 1900s-1940s
Objective: Perform a combined Preliminary Assessment and Site Inspection (PA/SI) via the Comprehensive Environmental Response, Compensation, and Liability Act (CERCLA)
Figure 2: Regional location of the Copper Age Mine [3]
Notes: spencer
BLM wants site analyzed because recreationalists and potential wildlife exposure
They need to know if there is contamination and if it’s severe enough to require removal
Chloride closest population, 2 miles northeast, 270 people
Operational from early to mid-1900s

## Slide 4
Figure 3: Aerial view of the Copper Age Mine [3]
North
Wash
Notes: spencer
The labels, including tailings and waste rock, were provided by BLM. The arrows near the southwestern area of the site depict the general slope and possible migration pathways (arroyo).

## Slide 5
Figure 4: Proposed sampling grid for Copper Age Mine
Notes: spencer
Grid sampling to minimize bias
Hotspot in north wash
Backgrounds

## Slide 6
Figure 5: Grid, hotspot, and background sampling locations map

## Slide 7: Field Work
Site Visit: January 19-20, 2018
Site Reconnaissance:
Identify potential hotspots
Observe site conditions for evidence of:
  Recreational activity
  Animal activity
Soil Sampling:
Grid (84)
Hotspot (7)
Background samples (3)
Figure 7: Human and Animal tracks found on site indicating recreational use. Photo Credit: Sarah Reddinger
Figure 6: Tire tracks found on site indicating human use. Photo Credit: Sarah Reddinger
Notes: spencer
Total of 94 samples
Decon
Gps points

## Slide 8: Laboratory Analysis: Sample Preparation
EPA Method 6200: Field Portable X-Ray Fluorescence Spectrometry for the Determination of Elemental Concentrations in Soil and Sediment [4]
Drying: 24 hours at 145 ℃
Sieving: Approximately 5-10 minutes; sample passed through 0.250 mm collected and bagged
Bagging: One-gallon freezer bag with a three by three grid
Figure 8: Mechanical shaker used to collect XRF samples. Photo Credit: Sarah Reddinger
Notes: sarah

## Slide 9: Laboratory Analysis: X-Ray Fluorescence
EPA Method 6200: Field Portable X-Ray Fluorescence Spectrometry for the Determination of Elemental Concentrations in Soil and Sediment [4]
Tasks Performed:
Sieved samples analyzed nine times with XRF
90-second readings of each grid square
Maximum and minimum readings removed, remaining averaged to identify contaminants of concern
Figure 9: Typical XRF analysis of samples. Photo credit: Sarah Reddinger
Notes: sarah
Task 3: Laboratory Analysis
3.4 Data Analysis
●Antimony – FAAS results were Non-detect [3]
●Arsenic - Ouliers consisted of values exceeding the lead to arsenic ratio of 10:1 [4]
○These were removed
○Help increase correlation coefficient to 0.41

## Slide 10: Preliminary Data Analysis
Contaminants of Concern: Arsenic, lead, and antimony were selected based on Arizona Non-Residential Soil Standards
Sample Selection: Twenty samples that best represented the arsenic, lead, and antimony concentration ranges
Samples then underwent further laboratory analysis at Colorado Plateau Analytical Lab on NAU campus
Table 1: Contaminants of concern concentration ranges, used in the selection of acid digestion samples
Concentration Range | Arsenic (mg/kg) | Lead (mg/kg) | Antimony (mg/kg)
Low | 0 | 25 | 0
Average | 450 | 46,610 | 250
High | 2,675 | 203,340 | 1,015
AZ Non-Residential Standard | 10 | 800 | 400
Notes: sarah
Task 3: Laboratory Analysis
3.4 Data Analysis
●Antimony – FAAS results were Non-detect [3]
●Arsenic - Ouliers consisted of values exceeding the lead to arsenic ratio of 10:1 [4]
○These were removed
○Help increase correlation coefficient to 0.41

## Slide 11: Laboratory Analysis: Flame Atomic Absorption Spectrophotometry Laboratory Analysis: Flame Atomic Absorption Spectrophotometry
Figure 10: Carl Haskie preparing samples for acid digestion. Photo Credit: Laura Garcia
Sample Preparation: Acid Digestion
Colorado Plateau Analytic Lab Protocol: Total Phosphorus in Microwave Digests [5]
Third-Party Analysis: CPAL
Twenty samples underwent acid digestion, followed by Flame Atomic Absorption Spectrophotometry
Notes: Carl
CPAL located at NAU

## Slide 12: Laboratory Analysis: Flame Atomic Absorption Spectrophotometry
Sample Preparation: Acid Digestion
Colorado Plateau Analytic Lab Protocol: Total Phosphorus in Microwave Digests [5]
Third-Party Analysis: CPAL
Twenty samples underwent acid digestion, followed by Flame Atomic Absorption Spectrophotometry
Figure 11: FAAS Instrument in the CPAL at Wettaw Biology Building. Photo Credit: Carl Haskie
Notes: carl

## Slide 13: Data Analysis: Arsenic Correlation
Outliers: Samples with lead to arsenic ratios equal or greater than 10:1 [4]
Correlation Coefficient (R): 0.64
Represents the relationship between FAAS and XRF data
Data Distribution:
Initially lognormally distributed
Log transformation to acquire normal distribution
Figure 12: Normal distribution of log transformed arsenic soil concentration using corrected XRF data
Notes: carl

## Slide 14: Data Analysis: Lead Correlation
Raw XRF data not included due to inconsistencies; only FAAS data was used
XRF Interferences:
Emission overlap with arsenic
Peak overlap with iron [6]
Correlation Coefficient (R): N/A
Data Distribution:
Binomial distribution after log transformation with raw XRF data
FAAS data used instead
Figure 13: Lognormally transformed normal distribution of FAAS lead data
Notes: carl

## Slide 15: Data Analysis: Antimony Correlation
Non-detect in all FAAS results; only XRF data was used
Interference: Microwave acid digestion method found to be inefficient for antimony extraction [7]
Correlation Coefficient (R): N/A
XRF Data Distribution:
Initially lognormally distributed
Log transformation to acquire normal distribution
Figure 14: Lognormally transformed normal distribution of antimony soil samples
Notes: carl

## Slide 16: Data Analysis: Concentration Levels
Normally Distributed Data:
50% Concentration: Average of the applied data
95% Concentration: 50% concentration plus two standard deviations
Table 2: 50% and 95% Concentrations for the Contaminants of Concern
 | AZ Non-Residential Soil Remediation Levels (mg/kg) | 50% Concentration (mg/kg) | 95% Concentration (mg/kg)
Arsenic | 10 | 186 | 1,070
Lead | 800 | 3,245 | 15,800
Antimony | 400 | 176 | 732
Notes: carl

## Slide 17
Notes: spencer

## Slide 18
Notes: spencer

## Slide 19
Notes: spencer

## Slide 20: Risk Assessment: Exposure Scenarios
Chronic Daily Intake (mg/kg-day): Carcinogenic and non-carcinogenic calculated.
Cancer Slope Factor for carcinogenic risk
Reference Dose for non-carcinogenic risk
Table 3: Exposure Scenarios Risk Summary for 50% Concentrations
 | Recreational Adult | Recreational Child | 1-Year Worker
Arsenic Non-Carcinogenic Risk Hazard Quotient | 0.03 | 0.07 | 0.54
Arsenic Carcinogenic Risk | 1.4E-4 | 9.3E-5 | 1.2E-4
Antimony Non-Carcinogenic Risk Hazard Quotient | 0.02 | 0.05 | 0.38
Antimony Carcinogenic Risk | N/A | N/A | N/A
Notes: sarah
HQ not above 1

## Slide 21: Risk Assessment: Exposure Scenarios
Chronic Daily Intake (mg/kg-day): Carcinogenic and non-carcinogenic calculated
Cancer Slope Factor for carcinogenic risk
Reference Dose for non-carcinogenic risk
Table 4: Exposure Scenarios Risk Summary for 95% Concentrations
 | Recreational Adult | Recreational Child | 1-Year Worker
Arsenic Non-Carcinogenic Risk Hazard Quotient | 0.20 | 0.41 | 3.13
Arsenic Carcinogenic Risk | 8.4E-4 | 5.3E-4 | 6.7E-4
Antimony Non-Carcinogenic Risk Hazard Quotient | 0.10 | 0.21 | 1.61
Antimony Carcinogenic Risk | N/A | N/A | N/A
Notes: sarah
HQ not above 1

## Slide 22: Risk Assessment: Adult Lead Model
US EPA Adult Lead Model (ALM): Analyzed adult lead blood levels (PbB) for recreationalists and workers [9]
Recommended Lead Blood Level (PbB): < 5 μg/dL
 | Recreational Adult | 1-Year Worker
Soil Ingestion Rate (g/day) | 0.1 | 0.1
Exposure Frequency (days/year) | 14 | 250
50% Adult PbB (ug/dL) | 1.5 | 11.6
95% Adult PbB (ug/dL) | 3.9 | 52.9
Table 5: Adult lead modeling exposure scenarios for recreational adult and 1-year worker
Notes: sarah
Recreational adult: 14 day camping limit by blm
1-year worker: remediation scenario for site

## Slide 23: Risk Assessment: Child Lead Exposure
Integrated Exposure Uptake Biokinetic Model (IEUBK): Assesses blood level concentration in children under 7 years of age
Recommended Lead Blood Level: <10 μg/dL and < 5% probability [8]
Figure 15: IEUBK Model Blood Lead Concentration for 50% lead Concentration
50% Concentration: 0.24% above recommended level
95% Concentration: 6.4% above recommended level [8]
Notes: laura
Mention different method for arsenic and antimony
Point out Red line
Not applicable for short term so it was corrected

## Slide 24: Risk Assessment: Child Lead Exposure
Integrated Exposure Uptake Biokinetic Model (IEUBK): Assesses blood level concentration in children under 7 years of age
Recommended Lead Blood Level: <10 μg/dL and < 5% probability [8]
Figure 16:IEUBK model blood lead concentration for 95% lead concentration
50% Concentration: 0.24% above recommended level
95% Concentration: 6.4% above recommended level [8]
Notes: laura
Mention different method for arsenic and antimony

## Slide 25: Risk Assessment: Ecological
EPA Risk Management Criteria [10]
Average XRF concentrations were compared to 15 elements and their respective Ecological Soil Screening Levels
All Copper Age Mine sample exceedances are highlighted
Table 6: Copper Age Mine soil concentrations compared to the EPA soil screening levels (mg/kg) weight in soil).
Notes: laura

## Slide 26
Notes: laura
Project Management is

## Slide 27: Staff Cost
The hourly rates cover overhead and benefits for each position.
Senior Engineer: $125/Hour
Total Hours: 128
Engineer: $80/Hour
Total Hours: 200
Associate Engineer: $40/Hour
Total Hours: 247
Technician: $35/Hour
Total Hours: 256
Total Staffing Cost: $50,840
Major Task | Senior Engineer | Engineer | Associate Engineer | Technician
Work Plan | 12 | 24 | 28 | 20
Field Work | 36 | 70 | 64 | 64
Lab Analysis | 10 | 24 | 75 | 92
Risk Assessment | 10 | 12 | 8 | 10
PA/SI Report | 30 | 28 | 46 | 44
Project Management | 30 | 42 | 26 | 26
Staff Total: | 128 | 200 | 247 | 256
Cost: | $16,000 | $16,000 | $9,880 | $8,960
Notes: laura
Staff justifications/responsibilities
Senior Engineer is responsible for overseeing the entire process of the project, including critical decisions and overall approach
Engineering is responsible for more day-to-day operations, and overseeing other members of the team
The primary difference between the EIT and Tech is the Tech is more focused on lab work

## Slide 28: Total Cost
Cost Description | Final Costs | Proposed Costs
Personnel | $50,840 | $61,730
Travel | $925 | $925
Material | $2,707 | $2,707
Subcontractor | $385 | $840
Training | $2,600 | $2,600
Equipment | $1,560 | $1,560
Total Costs: | $59,017 | $70,362
The subtotal costs for each cost description with the total cost.
Personnel: Staffing costs.
Travel: Hotel, per diem, and van rental.
Materials: Sampling and lab work supplies.
Subcontractor: Colorado Plateau Analytical Lab services quote.
Training: XRF and 40-hour HAZWOPER.
Equipment: Includes the XRF instrument, GPS unit, and camera.
Total Cost: $59,017
Notes: laura
Staff justifications/responsibilities
Senior Engineer is responsible for overseeing the entire process of the project, including critical decisions and overall approach
Engineering is responsible for more day-to-day operations, and overseeing other members of the team
The primary difference between the EIT and Tech is the Tech is more focused on lab work

## Slide 29: Acknowledgements
Eric Zielske, P.E., Client, Bureau of Land Management
Bridget Bero, Ph.D., P.E., Technical Advisor
Alarick Reiboldt, MEng, E.I.T., Grading Instructor, Advice Giver
Josue Juarez, Graduate Student Assistance
Adam Bringhurst, MEng, E.I.T., CENE Lab Manager
Jeffrey Propster and Bryden Baker, Colorado Plateau Analytical Lab
Marty Mihay, Instrumentation Specialist
Josh Froyum, Ingram Lab
Notes: Travel includes: van rental, mileage, hotel, and per diems
Supplies:
  Sampling Materials: ziplocs, tyvek suits, gloves, gps unit, shovels, etc. +20% fee
  Analytical Materials and Lab Expendables: chemicals, safety glasses, lab coats, etc. +20% fee
  Equipment: Field sampling/monitoring, safety, lab equipment
  Training: XRF, HAZWOPER
  Subcontracting: $35/sample, 20 samples. +20% fee

## Slide 30: References
[1] "El Oro", Arizona Department of Mines and Mineral Resources File Data.
[2] Arizona State Parks and Trails, "Arizona State Parks," [Online]. Available: https://azstateparks.com/find-a-park/.
[Accessed 27-11-2017].
[3] Google Earth Pro 2017. 2017.
[4] "METHOD 6200 FIELD PORTABLE X-RAY FLUORESCENCE SPECTROMETRY FOR THE
DETERMINATION OF ELEMENTAL CONCENTRATIONS IN SOIL AND SEDIMENT", US EPA, 2007.
[5] Lachat method 13-115-01-B, Total P, Kjeldahl digests, Copper catalyst, Rev. 26-Oct-06.
[6] "Common Causes of Lead Interference Using XRF", XOS, 2013.
[7] M. Tighe, P. Lockwood, S. Wilson and L. Lisle, "Comparison of Digestion Methods for ICP-OES Analysis of a
Wide Range of Analytes in Heavy Metal Contaminated Soil Samples with Specific Reference to Arsenic and
Antimony", Communications in Soil Science and Plant Analysis, vol. 35, no. 9-10, pp. 1369-1385, 2004.
[8] TRW Lead Committee, “Training on the IEUBK Model”, US EPA. [Online]. Available:
https://semspub.epa.gov/work/11/176285.pdf
[9] "Lead at Superfund Sites: Software and Users' Manuals | US EPA", US EPA, 2017. [Online]. Available:
https://www.epa.gov/superfund/lead-superfund-sites-software-and-users-manuals.
[10] “Interim Ecological Soil Screening Level Documents”, US EPA. [Online]. Available:
https://www.epa.gov/chemical-research/interim-ecological-soil-screening-level-documents