## Slide 1
Signal Mill Preliminary Assessment/Site Investigation
Angelina Cruse, Wyatt La Fave, Anna Gorman, Ali Husain

## Slide 2: Project Introduction
Client: Bureau of Land Management (BLM)
Background: Signal Mill was a stamp mill used to process ores from the McCracken Mine.
Stamp mill: A machine that crushes ores by pounding instead of grinding.
Purpose: To provide the BLM with a Preliminary Assessment/Site Investigation (PA/SI) report, the first step of the Comprehensive Environmental Response, Compensation, and Liability Act (CERCLA) process to remediate Signal Mill [1].
1
Figure 1. Population of the Town of Signal

## Slide 3: Location
2
Figure 2. Location of Signal Mill.
Kingman
Signal Mill
Phoenix
Flagstaff

## Slide 4
Development of Sampling and Analysis Plan
  Sampling procedure
  Lab analysis procedure
  Proper documentation
Development of Health and Safety Plan
  Ensures health and safety on site
  Emergency response procedure
Figure 3. Rundown Structure at Signal Mill
3
Work Plan

## Slide 5: Field Sampling
Sampling occurred
January 18 - 19, 2019
82 soil samples collected
  3 Background
  5 Hotspot
  74 grid samples
Flora and Fauna Survey Completed on Site
Figure 4. Preparing for sampling.
Figure 6. Frog found on site
Figure 5. Soil sampling
4

## Slide 6
Figure 7. Original Sampling Grid.
Figure 8. Sampling Grid Showing Excluded Samples.
5
Signal Mill
Excluded Samples
Direction of Flow

## Slide 7: Drying and Sieving
Each sample was oven dried at 60 ℃ to prevent loss of mercury (EPA Method 200.8) [1].
Samples are sieved to the No. 40 sieve (deviation from EPA method 6200) [2].
6
Figure 9. Mechanical Shaker
Figure 10. No. 40 Sieve

## Slide 8: X-Ray Fluorescence Analysis
Figure 11. Sample Cups Prepared for Analysis
Figure 12. Sample Bags next to Finished XRF
7
Notes: Maximum weight that these cups can hold is approx around 21 grams.
The inner size of the cups are about 23 mm.

## Slide 9: X-Ray Fluorescence Analysis
Figure 13. Sample Cup in the Stand Ready for Analysis
Figure 14. Mobile Stand used in Analysis
8
Notes: I would include the other image that Angelina created with the arrows.

## Slide 10: X-Ray Fluorescence Data
Table 1. XRF Data
9
U – Uranium
Pb – Lead
As – Arsenic
Hg – Mercury
Zn – Zinc
Cu – Copper
Ni - Nickel
Above AZ Non-Residential Soil Standards
Above AZ Residential Soil Standards
Residential: areas in which constant exposure occurs (neighborhoods)
Non-Residential: areas not intended for development

## Slide 11: X-Ray Fluorescence Data
Table 2. XRF Data
Fe – Iron
Mn – Manganese
V – Vanadium
Ba – Barium
Sb – Antimony
Sn – Tin
Cd – Cadmium
Ag - Silver
10
Above AZ Non-Residential Soil Standards
Above AZ Residential Soil Standards
Residential: areas in which constant exposure occurs (neighborhoods)
Non-Residential: areas not intended for development

## Slide 12: Contaminants of Concern
Human Health Risk
  Lead
  Arsenic
  Manganese
Ecological Health Risk
  Lead
  Zinc
  Copper
  Manganese
  Vanadium
  Nickel
  Barium
  Cadmium
  Silver
11

## Slide 13
Above 800 mg/kg
400 mg/kg < X < 800 mg/kg
Below 400 mg/kg
Figure 15. Lead Concentrations (HH Criteria)
30,033 mg/kg of Lead
2,756 mg/kg of Lead
LEGEND
37 mg/kg of Lead
12

## Slide 14
30,033 mg/kg of Lead
2,756 mg/kg of Lead
37 mg/kg of Lead
>120 mg/kg - affecting plants
>56 mg/kg - affecting mammals
>11 mg/kg - affecting avian wildlife
< 11 mg/kg – doesn’t affect any biota
LEGEND
Figure 16. Lead Concentrations (Eco Criteria)
13

## Slide 15: Acid Digestion
Table 3. Organization of Choosing Samples for Digestion
14
Above AZ Non-Residential Soil Standards
Above AZ Residential Soil Standards
Samples Chosen for Acid Digestion

## Slide 16: Acid Digestion
Figure 17. Setup for Acid Digestion in the Fume Hood
Figure 18. Acid Digestion of Samples
15

## Slide 17: Data Correlation
Figure 19. Lead Natural Log Distribution
Table 5. 95% and 50% Exposure Point Concentrations (EPC)
16
Contaminant | 50% EPC (mg/kg) | 95% EPC (mg/kg)
Arsenic | 3.2 | 10.1
Manganese | 1662.5 | 3298.7
Lead | 2023.4 | 16425.6
Table 4. Contaminant Correlation Values
Contaminant | R-Value
Lead | 0.9859
Arsenic | 0.8387
Manganese | 0.9512

## Slide 18: Human Health Risk Assessment
Most probable exposure scenarios:
Recreational (camping)
  Adult
  Child
  Exposure frequency: 14 days/year
  Exposure duration: 10 years
Worker
  Adult
  Exposure Frequency: 350 days/year
  Exposure duration: 1 year
17
Scenario | Person | EPC | Ingestion Rate (mg soil / day)
Camping | Adult | 50% | 100
Camping | Adult | 95% | 100
Camping | Child | 50% | 200
Camping | Child | 95% | 200
Worker | Adult | 50% | 50
Worker | Adult | 95% | 100
Table 6. Ingestion Rates used for 50% and 95% Exposure Point Concentrations (EPC)

## Slide 19
Hazard Index
(Non-carcinogenic)
Cancer Risk
(Carcinogenic)
Hazard:
HI > 1
Used for:
Arsenic, Manganese
Hazard:
Risk > 10-6
Used for:
Arsenic
HI: Hazard Index
(unitess)
CDI: Chronic Daily Intake (mg/[kg⋅day])
RfD: Reference Dose (mg/[kg⋅day])
CSF: Cancer Slope Factor ([kg⋅day]/mg)
18
Human Health Risk Assessment

## Slide 20: Human Health Risk Assessment
Chronic Daily Intake
CDI: chronic daily intake (mg/[kg×day])
CS: chemical concentration in soil (mg/kg)
IR: ingestion rate (mg soil/day)
CF: conversion factor for soil 10-6 (kg/mg)
FI: fraction ingested
EF: exposure frequency (days/years)
ED: exposure duration (years)
BW: body weight (kg)
AT: averaging time (days)
19
Notes: Do we need?

## Slide 21: Human Health Risk Assessment - Arsenic
Table 7. Arsenic Human Health Risk Assessment Results
20
CS – Concentration of Soil
IR – Ingestion Rate (mg soil/day)
CDI – Chronic Daily Intake (mg/kg·day)
HI – Hazard Index
Scenario | Person | CS | IR | CDI (mg/kg·day) | HI | Cancer Risk
Camping | Adult | 50% | 95% | 1.76E-08 | 0.000059 | 2.64 E-08
Camping | Adult | 95% | 95% | 5.53E-08 | 0.000184 | 8.30 E-08
Camping | Child | 50% | 95% | 7.56E-08 | 0.000249 | 1.12 E-07
Camping | Child | 95% | 95% | 2.35E-07 | 0.000783 | 3.52 E-07
Worker | Adult | 50% | 50% | 2.20E-06 | 0.007329 | 3.30 E-06
Worker | Adult | 95% | 95% | 1.38E-05 | 0.046119 | 2.08 E-05

## Slide 22: Human Health Risk Assessment - Manganese
Table 8. Manganese Human Health Risk Assessment Results
21
CS – Concentration of Soil
IR – Ingestion Rate (mg soil/day)
CDI – Chronic Daily Intake (mg/kg*day)
HI – Hazard Index
Scenario | Person | CS | IR | CDI (mg/kg·day) | HI
Camping | Adult | 50% | 95% | 9.11E-06 | 0.0000651
Camping | Adult | 95% | 95% | 1.81E-05 | 0.0001291
Camping | Child | 50% | 95% | 3.86E-05 | 0.0002761
Camping | Child | 95% | 95% | 7.67E-05 | 0.0005477
Worker | Adult | 50% | 50% | 1.14E-03 | 0.0081338
Worker | Adult | 95% | 95% | 4.52E-03 | 0.0322773

## Slide 23: Human Risk Assessment- Lead (Adults)
Table 9. Adult Lead Human Health Risk Assessment Results
*Risk probability is based on exceeding 5 PbB μg/dl
Scenario | Person | EPC | CS (mg/kg) | IR (mg/day) | Risk
Camping | Adult | 50% | 2023 | 100 | 0.15%
Camping | Adult | 95% | 16426 | 100 | 23.37%
Worker | Adult | 50% | 2023 | 50 | 46.30%
Worker | Adult | 95% | 16426 | 100 | 100%
22
CS – Concentration of Soil
EPC- Exposure Point Concentration
IR – Ingestion Rate (mg soil/day)
PbB- Lead Blood Concentration

## Slide 24: Human Risk Assessment- Lead (Children)
Table 11. IEUBK Lead 95% EPC Human Health Risk Assessment Results
23
Child Age Range (years) | Blood Pb (μg/dL)
0.5-1 | 3.0
1-2 | 2.6
2-3 | 2.3
3-4 | 2.2
4-5 | 2.0
5-6 | 1.9
6-7 | 1.8
Child Age Range (years) | Blood Pb (μg/dL)
0.5-1 | 12.9
1-2 | 11.5
2-3 | 10.1
3-4 | 9.7
4-5 | 9.4
5-6 | 9.0
6-7 | 8.4
Table 10. IEUBK Lead 50% EPC Human Health Risk Assessment Results

## Slide 25
Figure 20. 50% EPC IEUBK Probability Distribution
Figure 21. 95% EPC IEUBK Probability Distribution
24

## Slide 26
Table 12. Eco Contaminant Level Standards
Table 13. Samples Exceeding Contaminant Levels for Eco Risk
25
Ecological Risk Assessment
Notes: Fix table to format like others, use average font

## Slide 27: Ecological Risk Assessment
Endangered Species
A - Arizona Cliffrose
B - Southwestern Willow Flycatcher
C - California Least Tern
Threatened Species
D - Desert Tortoise
E - Northern Mexican Gartersnake
Figure 22. Native Animal Species
26

## Slide 28: Ecological Risk Assessment
Bioaccumulation
  Plants uptake contaminated water flowing from the site
  Plants are the base of the food chain
Migration
  Site has a lot of hills
  Rainfall flows down towards Big Sandy
27
Figure 23. Desert Food Chain [3]

## Slide 29
28

## Slide 30
29

## Slide 31: Project Hours
Table 14. Proposed hours spent over the course of the project
Tasks | SENG | ENG | EIT | LAB
Task 1 Work Plan (Cumulative) | 8 | 24 | 24 | 0
Task 1.1. SAP | 4 | 12 | 12 | 0
Task 1.2 HASP | 4 | 12 | 12 | 0
Task 2. Field Sampling | 2 | 23 | 23 | 0
Task 3 Analysis (Cumulative) | 2 | 23 | 23 | 120
Task 3.1 Drying & Sieve Analysis | 0 | 0 | 0 | 40
Task 3.2 XRF Analysis | 0 | 0 | 0 | 40
Task 3.3 Acid Digestion | 0 | 0 | 0 | 16
Task 3.4 Data Correlation | 2 | 23 | 23 | 12
Task 4 Risk Assessment | 16 | 48 | 40 | 0
Task 4.1 Human Health Risk Assessment | 8 | 24 | 20 | 0
Task 4.2 Ecological Risk Assessment | 8 | 24 | 20 | 0
Task 5 Project Impact | 2 | 4 | 2 | 0
Task 6 Project Management (Cumulative) | 142 | 116 | 78 | 16
Cumulative Hours | 172 | 238 | 190 | 136
Sum of Hours | 736 |  |  | 
30
SENG - Senior Engineer
ENG - Professional Engineer
EIT- Engineer in Training
LAB – Laboratory Technician

## Slide 32: Project Hours
Table 15. Total Hours Spent Over the Course of the Project
Tasks | SENG | ENG | EIT | LAB
Task 1 Work Plan (Cumulative) | 11 | 21 | 20 | 0
Task 1.1. SAP | 5.5 | 10.5 | 10 | 0
Task 1.2 HASP | 5.5 | 10.5 | 10 | 0
Task 2. Field Sampling | 22.5 | 45 | 67.5 | 0
Task 3 Analysis (Cumulative) | 2.5 | 11.5 | 11.5 | 225
Task 3.1 Drying & Sieve Analysis | 0 | 0 | 0 | 60.25
Task 3.2 XRF Analysis | 1.5 | 8 | 9 | 100.25
Task 3.3 Acid Digestion | 0 | 0 | 0 | 64.5
Task 3.4 Data Correlation | 1 | 3.5 | 2.5 | 0
Task 4 Risk Assessment | 7.5 | 9.5 | 5.5 | 0
Task 4.1 Human Health Risk Assessment | 6.5 | 7.5 | 2.5 | 0
Task 4.2 Ecological Risk Assessment | 1 | 2 | 3 | 0
Task 5 Project Impact | 4 | 3 | 0 | 0
Task 6 Project Management (Cumulative) | 78.5 | 68 | 55 | 0
Cumulative Hours | 126 | 158 | 159.5 | 225
Sum of Hours | 668.5* |  |  | 
*Under by 67.5 hours
31
SENG - Senior Engineer
ENG - Professional Engineer
EIT- Engineer in Training
LAB – Laboratory Technician

## Slide 33: Cost of Engineering Services
Table 16. Original Cost Estimate for the Project
32

## Slide 34: Cost of Engineering Services
Table 17. Total Cost of Engineering Services for the Project
33

## Slide 35: Project Impacts
Economic
  If remediation occurs, tax payer money would help fund the project
  Create new jobs for remediation
Environmental
  Ecological risk present
  If remediated, migration down the Big Sandy River would be mitigated
Social
  Recreational users are affected by lead contamination on site
Figure 24. Big Sandy River
34

## Slide 36: References
[1] U.S. EPA. “EPA Method 200.8: Determination of Trace Elements in Waters and Wastes by Inductively Coupled Plasma-Mass Spectrometry” Washington, DC. 2007
[2] U.S. EPA. “ SW-846 Test Method 6200: Field Portable X-Ray Fluorescence Spectrometry for the Determination of Elemental Concentrations in Soil and Sediment,” Washington, DC. 2007
[3] Northern Arizona University. Desert Food Chain. Available: https://www2.nau.edu/lrm22/lessons/food_chain/food_chain.html
35

## Slide 37
Chart: Lead Correlation Data
| 28.135714285714283 | 116.14999999999999 | 162.57000000000002 | 336.26714285714286 | 681.04250000000002 | 851.52571428571434 | 1271.7800000000002 | 1773.5850000000003 | 1998.1928571428568 | 2755.5085714285715 | 3411.1233333333334 | 4010.9785714285708 | 5267.6842857142847 | 5787.045714285714 | 7352.0214285714274 | 9429.5414285714305 | 13562.922857142856 | 15430.071428571431 | 21953.809999999998 | 26844.940000000002
 | 56 | 86 | 180 | 338 | 1146 | 1195 | 1195 | 2345 | 2484 | 3478 | 5521 | 5618 | 6030 | 6599 | 6629 | 9242 | 12176 | 15524 | 23334 | 22865
36
Figure 25. Lead Correlation Data