## Slide 1: Traffic Sign Cleaning
Abdalla
Saad
Abdulrahman
Mohammed
Mosaad
Abdullah
DEFINING NEW WAYS

## Slide 2: OVERVIEW
Project Description
Requirements
Design Solution
Design Making
System Manufacturing and Assembly
Design Of Manufacturing and Assembly (DFMA)
Testing
Budget
Future Work
References
Appendix

## Slide 3: PROJECT DESCRIPTION
Traffic Signs play an important role in controlling the traffic
Traffic Signs always uses sharp color, see from the long distance
Traffic Sign Board on the highways need to clean
Drivers need to see the instructions clearly
Traffic flow on highways cannot disrupt
Design a system that can clean traffic sign boards
  Without Disturbing the traffic flow
Client
  Dr. Hesam Moghaddam

## Slide 4: CUSTOMER REQUIREMENTS
Customer Requirements | Weightage
Do not interrupt the flow of traffic | 9
Failsafe | 8
Collect Water Drops | 7
Clean in short time | 6
Clean without damaging the coating | 5
Safe to Operate | 4
Cost within budget | 3
Durable and Robust Design | 2
Reliable Design | 1

## Slide 5: ENGINEERING REQUIREMENTS
Engineering Requirements | Target Values | Tolerance | Justification
Flight Time | 20 minutes |  | 20 minutes have given, 5 minutes tolerance so that it can work easily in that limit
Height of Flight | 100 feet |  | The normal height required is around 100 feet so tolerance is 10 feet above or below this value
Water tank | 20 liters |  | 20 liter of water is enough to clean boards, and 3 liter of tolerance can easily work for it
Device Weight | 30 lb. |  | 30 lb of device is enough to lift up and 5 lb of tolerance to bear the extra load
Reliable in temperature | -10C to 40C |  | High range of temperature variation can wear in this range with tolerance of 5 degrees at each point
Durable | 2200 MPa |  | Bear the shear stress of 2200 MPa to show durability, 2200 MPA is high value so tolerance range is high as 200.
Long Power Backup | 30 Mins |  | Power require to run the drone and reel must be 30 minutes while the tolerance is 5 minutes
Failsafe rotation speed | 25 rpm |  | The rotation of reel must 25 rpm with the tolerance of 5 rpm.
Hose Height | 65 ft |  | Hose will provide the height of 65 feet with the tolerance of 5 feet.
Engineering Requirements | Target Values | Tolerance | Justification
Flight Time | 20 minutes |  | 20 minutes have given, 5 minutes tolerance so that it can work easily in that limit
Height of Flight | 100 feet |  | The normal height required is around 100 feet so tolerance is 10 feet above or below this value
Water tank | 20 liters |  | 20 liter of water is enough to clean boards, and 3 liter of tolerance can easily work for it
Device Weight | 30 lb. |  | 30 lb of device is enough to lift up and 5 lb of tolerance to bear the extra load
Reliable in temperature | -10C to 40C |  | High range of temperature variation can wear in this range with tolerance of 5 degrees at each point
Durable | 2200 MPa |  | Bear the shear stress of 2200 MPa to show durability, 2200 MPA is high value so tolerance range is high as 200.
Long Power Backup | 30 Mins |  | Power require to run the drone and reel must be 30 minutes while the tolerance is 5 minutes
Failsafe rotation speed | 25 rpm |  | The rotation of reel must 25 rpm with the tolerance of 5 rpm.
Hose Height | 65 ft |  | Hose will provide the height of 65 feet with the tolerance of 5 feet.

## Slide 6: DESIGN SOLUTION
The design decided to use drone
10 propellers are using on the drone to fly in the air
Pipe Structure is using to build the drone
Nozzle are using on the design to shower water on sign boards
Soft brush rollers are using to wipe the boards
Water is supplying to the drone from ground tank
Hose is connecting with the drone to provide fail-safe

## Slide 7: DESIGN SOLUTION
Final Design CAD Model

## Slide 8: DESIGN MAKING
Flight Time – 20 minutes
  The propellers using in the drone are high torque and high speed motors providing high initial velocity
Height of Flight – 100 feet
  Even though we need the maximum height of 70 feet

## Slide 9: DESIGN MAKING
Water Tank Capacity – 20 liters
Device Weight – 30 lb.

## Slide 10: DESIGN MAKING
Reliable in Temperature – -10C to 40C
  ABS plastic can withstand up-to 60C easily
  Motors can withstand up-to 65C easily
  Arduino Controller can withstand up-to 60C easily
Durable – 2200 MPa
  ABS plastic has young's modulus of 2.4 GPa
  Project need 2200 MPa, where

## Slide 11: DESIGN MAKING
Long Power Backup – 30 mints
Failsafe Rotation Speed – 25 rpm
  The motor connected with the reel will rotate more than 25 rpm as it is ¼ hp 12 V dc motor with the RPM of 2600

## Slide 12: DESIGN MAKING
Hose Height – 65 feet
These engineering decision fulfills the engineering requirements by the selected design
On the basis of these calculations the decision has taken for the selected design

## Slide 13: BACKUP DESIGN DECISION
For Backup design, remove the hose, water tank
Connect the battery with the drone
Place the bottle holder
Fly the drone with the same propellers and same motors

## Slide 14: SYSTEM MANUFACTURING
COMPONENTS DETAILS

## Slide 15: SYSTEM MANUFACTURING
Components Details
Arduino UNO R3
Propeller Motor
Soft Fabric Brush
Reel Engine

## Slide 16: SYSTEM ASSEMBLY
Assembly Time for Drone is 1200 seconds
Number of parts are 56
  20 Screws
  2 Nut Bolts
  6 Elbows

## Slide 17: DESIGN OF ASSEMBLY (DFA)
Assembly Time for Drone is1200 seconds
Number of parts are 56
  20 Screws
  2 Nut Bolts
  6 Elbows
Assembly Time drop to 300 seconds
Number of parts reduced to 32
  0 Screws
  2 Hooks
  2 Elbows
ORIGINAL DESIGN
RE-DESIGN

## Slide 18: DESIGN OF MANUFACTURING (DFM)
Pipe Connect Propeller Original
Re-design for pipe
Pipe Joint Original
Pipe Joint Re-Design

## Slide 19: DESIGN OF MANUFACTURING AND ASSEMBLY (DFMA)
Description | Original Design | Redesign | Improvements %
Assembly Time Hours | 1.5 | 0.3 | 80
No. of Different Parts | 26 | 4 | 84.62
Total No. of Parts | 56 | 32 | 42.8
Cost | $902 | 780 | 13.5%
Labor Cost | $200 | $165 | 17.5%

## Slide 20: FMEA
Part # and Functions | Potential Failure Mode | Potential Effect(s) of Failure | Severity (S) | Potential Causes and Mechanisms of Failure | Occurrence (O) | Current Design Controls Test | Detection (D) | RPN | Recommended Action
1 Controller |  |  |  |  |  |  |  |  | 
1.1 Controller Brun | Burning of Controller | Disconnection with Drone | 7 | 1. Bad quality of controller | 4 | 1. Over Voltage Test | 4 | 112 | Check the quality of controller
2 Motor |  |  |  |  |  |  |  |  | 
2.1 Shaft | Bending of Shaft, Breakage of Shaft | wait for new shaft, cost increased | 7 | 1.Bad quality due to molding, 2. poor quality shaft is used | 4 | 1.Bad seeding, Poor Quality aluminum | 6 | 168 | Test various qualities if pipes available at same cost
3 Arduino |  |  |  |  |  |  |  | 0 | 
3.1 Arduino Board | Burning of board | shorting of circuit | 5 | 1. unsecure circuit lining | 7 | 1. Over Voltage Test | 5 | 175 | Check the circuit lining
4 Power Adopter |  |  |  |  |  |  |  | 0 | 
4.1 Over voltage | Producing over voltage causing other devices to burns | Over Current | 5 | Bad quality of wiring | 5 | 1. Over Voltage Test | 6 | 150 | Check quality of wire copper

## Slide 21: TESTING PROCEDURES
Flight Time – 20 minutes
  Need the timer to test this ER and see if it has fulfilled
  Timer is available in the mobile
Height of Flight – 100 feet
  Barometer and GPS device will use to determine the height of drone
  Barometer is available in the mechanical lab, GPS is present in the Arduino
Water Tank Capacity – 20 liters
  Use the water bottle of 20 liters and fill the tank to see if water tank can store 20 liters or not

## Slide 22: TESTING PROCEDURE
Device Weight – 30 lb.
  Weight machine need to measure the weight of device
  Drone will place over the machine to test
  Weight machine is available in the mechanical lab
Reliable in Temperature – -10C to 40C
  Put the device in the controlled temperature room
  Test it in both highest temperature and lowest temperatures
  Available in the chemistry lab

## Slide 23: TESTING PROCEDURE
Durable – 2200 MPa
  Put the structure under stress by applying the external force
  The equipment need to do is stress applying machine and test the structure
  The equipment is available in the mechanical lab
Long Power Backup – 30 mints
  To test it, timer watch need to see if it consistently get the power for 30 minutes
  Timer is available in the mobile

## Slide 24: TESTING PROCEDURE
Failsafe Rotation Speed – 25 rpm
  The RPM of motor can test by through tachometer.
  Tachometer can available in the mechanical lab
Hose Height – 65 feet
  Hose height can test through the meter scale
  Meter scale can easily available in the civil lab

## Slide 25: BUDGET
Part Name | Qty | Unit Cost | Cost
6 mm Motor | 10 | $25.07 | $250.72
Steel Sheet | 1 | $38.32 | $38.32
Arduino | 1 | $3.49 | $3.49
Controller | 1 | $27.99 | $27.99
Reel Motor | 1 | $78.28 | $78.28
Hose | 1 | $29.50 | $29.50
Screws | 50 | $0.02 | $1.14
Pipe | 8 | $22.31 | $178.50
Electric Power Wire | 1 | $11.96 | $11.96
Jumper Wires | 4 | $1.00 | $4.00
Wheels | 2 | $1.23 | $2.45
Propeller | 10 | $6.06 | $60.55
Brushes | 2 | $6.10 | $12.20
Nozzles | 5 | $4.02 | $20.10
Reel | 1 | $50.00 | $50.00
Glue | 2 | $1.22 | $2.44
Total |  |  | $771.64
Total incl. tax |  |  | $902.82

## Slide 26: Budget
Components Price | $902
Manufacturing Cost | $65
Labor Cost | $200
Total Cost | $1167

## Slide 27: FUTURE WORK
In future, the improvement need to make in the design
It can carry extra load in the air
Drone will become autonomous
  Detect the Sign Boards
  Clean them without the use of Remote
  Auto-refilling of water from the tank
  Nozzle operation will become autonomous

## Slide 28: REFERENCES
[1] B. Marian, “Investigation of hydraulic fitting losses”, available [online], https://www.researchgate.net/publication/325338468_Investigation_of_hydraulic_fitting_losses
[2] M. Santosh, “Compartive study for Wiper Control System Using MATLAB”, available [online], https://www.researchgate.net/publication/335524435_Comparative_Study_for_Wiper_Control_Systems_using_MATLAB_Tools
[3] P. Imade, “Design, Production, and Testing”, available [online], https://www.researchgate.net/publication/320244094_Design_Production_and_Testing_of_a_Single_Stage_Centrifugal_Pump
[4] B. Mohammed”, Power Supply Architectures for Drones”, available [online], https://www.researchgate.net/publication/336669179_Power_Supply_Architectures_for_Drones_-_A_Review
[5] L. Leo, “Working Principle of Arduino and its tools”, available [online], https://www.researchgate.net/publication/326316390_WORKING_PRINCIPLE_OF_ARDUINO_AND_USING_IT_AS_A_TOOL_FOR_STUDY_AND_RESEARCH

## Slide 29: APPENDIX – BILL OF MATERIALS
Part # | Part Name | Qty | Description | Functions | Material | Dimensions | Cost
1 | 6 mm Motor | 10 | Rotate the Propellers | Rotate the propellers | Steel | 1.2 x 1 in | $250.72
2 | Steel Sheet | 1 | For Water Tank | Make the Water Tank | Steel | 100 x 100 mm | $38.32
3 | Arduino | 1 | Control the Drone | Pass the signals to each part | Silicon | 4 in x 4 in | $3.49
4 | Controller | 1 | Control the Remotely | Connect with Arduino to pass signals | Plastic | 6 x 4 in | $27.99
5 | Reel Motor | 1 | Rotate the reel | Provide Failsafe operation | Iron Copper | 15 in x 8 in | $78.28
6 | Hose | 1 | Connect with Drone and Reel | Provide Failsafe operation | plastic | 4 x 2 in | $29.50
7 | Screws | 50 | Make the connections | Hold the parts | Steel | 0.5 x 0.1 in | $1.14
8 | Pipe | 8 | Make drone structure | Design the Structure | ABS Plastic | 50 feet | $178.50
9 | Electric Power Wire | 1 | Provide Power | Connect the power with the Arduino | Copper | 10 feet | $11.96
10 | Jumper Wires | 4 | Connect between the parts | Make all the connection for supply | Copper | 6 x 0.1 in | $4.00
11 | Wheels | 2 | To move the device | Assist in moving by reducing friction | Rubber | 6 in | $2.45
12 | Propeller | 10 | Rotate the Propellers | Lift the drone with the propeller | Plastic | 4 in x 2 in | $60.55
13 | Brushes | 2 | Clean the boards | Rotate and clean the water from board | Fabric | 4 in x 2 in | $12.20
14 | Nozzles | 5 | Shower the water | Throw water on the boards | Steel | 3 in | $20.10
15 | Reel | 1 | Rotate quickly | Provide Failsafe operation | Steel | 20 in x 15 in | $50.00
16 | Glue | 2 | Make the connections of structure | fix the pipes and elbows | Chemical | 6 in | $2.44
Total |  |  |  |  |  |  | $771.64
Total incl. tax |  |  |  |  |  |  | $902.82

## Slide 30: FMEA
Part # and Functions | Potential Failure Mode | Potential Effect(s) of Failure | Severity (S) | Potential Causes and Mechanisms of Failure | Occurrence (O) | Current Design Controls Test | Detection (D) | RPN | Recommended Action
1 Controller |  |  |  |  |  |  |  |  | 
1.1 Controller Brun | Burning of Controller | Disconnection with Drone | 7 | 1. Bad quality of controller | 4 | 1. Over Voltage Test | 4 | 112 | Check the quality of controller
1.2 Controller Transmitter | Burning of transmitter | Disconnection with Drone | 6 | 1. Bad quality of transmitter | 4 | 1. Over Voltage Test | 4 | 96 | Check the quality of controller
1.3 Controller Receiver | Burning of Receiver | Disconnection with Drone | 6 | 1. Bad quality of receiver | 4 | 1. Over Voltage Test | 4 | 96 | Check the quality of controller
1.4 Controller Body | Breaking of Body | Cracks and bends | 4 | 1. Bad quality of controller | 3 | 1. Over Pressure Test | 3 | 36 | Check the quality of controller
1.5 Controller Board | Burning of board because of short circuit | Disconnection with Drone | 3 | 1. Bad quality of controller | 3 | 1. Over Voltage Test | 3 | 27 | Check the quality of controller
1.6 Controller battery | battery Dead | Disconnection with Drone | 4 | 1. Bad quality of battery cells | 4 | 1. Over Voltage Test | 4 | 64 | Check the battery quality
1.7 Controller Button | Button failure | Not working of specific function | 3 | 1. Bad quality of push button | 3 | 1. Over Pressure Test | 4 | 36 | Check the quality of button
1.8 Controller Handle | Handle stick motion failure | Not working the directions | 3 | 1. Bad quality of handle | 3 | 1. Over Pressure Test | 3 | 27 | Check the quality of handle
1.9 Controller Screen | Breaking of screen | No display | 3 | 1. Extra pressure and bad quality | 3 | 1. Over Pressure Test | 2 | 18 | Protect the screen
1.10 Controller Range | Failure of range abruptly | Low battery level | 3 | 1. Voltage excess and low level | 2 | 1. Over Voltage Test | 3 | 18 | Check the quality of battery
2 Motor |  |  |  |  |  |  |  |  | 
2.1 Shaft | Bending of Shaft, Breakage of Shaft | wait for new shaft, cost increased | 7 | 1.Bad quality due to molding, 2. poor quality shaft is used | 4 | 1.Bad seeding, Poor Quality aluminum | 6 | 168 | Test various qualities if pipes available at same cost
2.2 Motor Winding | Winding burn out | Cost increase | 8 | 1. bad quality of copper 2. poor windings 3. over voltage, over speed | 4 | 1. Speed test 2. Over voltage test | 5 | 160 | Check multiple motors and test them roguishly