## Slide 1: Honda EV Conversion Kit Capstone Initial Testing Results
Paul Howell, Wyatt Watson, Josh Hattaway, David Brooks, and Bryce Greenberg

## Slide 2: Design Requirements
Customer Requirement | Developed Engineering Requirement
CR1 - Battery life sufficient for average commuter | ER1 - Range greater than 100 miles
CR2 - Six or more batteries in vehicle | ER2 - Increase battery capacity greater than 40 kWh
CR3 - Consumer sellable (safe and durable) product | ER3 - Reduce cost of production ($)
CR3 - Consumer sellable (safe and durable) product | ER4 - Maximize power output 300 hp
CR3 - Consumer sellable (safe and durable) product | ER5 - Maximize torque output 250 ft-lb
CR4 - Lightweight | ER6 - Decrease weight less than 3000 lbs.
CR5 - Cooling system for electric motor | ER7 - Cool components to less than 200°F
CR6 - Compatibility with similar vehicle models | ER8 - Reduce number of mounts, 5 or less
Table 1: CR's and ER's
Joshua Hattaway

## Slide 3: Top Level Testing Summary
Experiment/Test | Relevant DRs
EX1 – Weight Test | CR4, ER6
EX2 – Battery Voltage Test | CR1, CR2, ER1, ER2
EX3 – Pre-Drive Electrical Test | CR3
EX4 – Pre-Drive Rigidity Test | CR3
EX5 – Range Test | CR1, CR2, ER1, ER2
EX6 – Production Process Test | CR3, ER3
EX7 – Compatibility Test | CR6, ER8
EX8 – Cooling Test | CR5, ER7
EX9 – Power Output Test | CR3, ER4
EX10 – Torque Output Test | CR3, ER5
Table 2: Testing overview
Ten tests planned
  8 for verifying Design Requirements
  2 for guaranteeing safety of drivers
Joshua Hattaway

## Slide 4
In-depth description of tests
> 25% complete
Majority of tests will be completed after final wiring
Completed tests:
  Weight
  Pre-drive electrical test (half completed)
  Production Process
  Fitment
  Battery Voltage
Detailed Testing Plans
Paul Howell

## Slide 5: Weight Test
Research
Research and determine weight of vehicle, original engine, and Tesla small drive unit.
Calculate
Calculate gross weight of assembled vehicle by adding together individual component weights.
Weigh
Weigh vehicle and compare to previously calculated. (Vehicle gained approximately 300 pounds, but more than doubled power)
Figure 1: Tesla motor
Figure 2: Batteries and mounts
Figure 3: Motor mounts
Paul Howell

## Slide 6: Pre-Drive Electrical Test
Paul Howell
Power on and check critical safety and operational components
  12 Volt System (Lights, Horn, etc) has been fully validated
  400 Volt System in progress
    External charger validated
    Battery connections validated
    Motor connections validated
    Main contactor validated
    On board charger in progress

## Slide 7: Production Process Test
BOM
Determine final Bill of Materials
Hardware Prices
Determine cost of hardware
Laser Cutting
Get sheet metal pieces laser cut.
Assembly Time
Time the process to fully assembly mounts.
Total Cost
Sum together all aspects of production.
David Brooks

## Slide 8: Fitment Test
David Brooks
Final test fit
Test final design into teams Honda Del Sol.
Second vehicle fitment
Confirm fitment in EG Civic
Third vehicle fitment
Confirm fitment in Acura Integra

## Slide 9: Battery Voltage Test
Figure 4: Testing voltage of battery module
Figure 5: Battery voltage reading
Wyatt Watson
Test voltage of each of the 6 LG Chem batteries with multimeter
  Ensure voltage levels meet manufacturer nominal motor requirements (275-420V, target of 400)
  Fully charged batteries: 6 x 60.1 V = 360.6V
Calculate capacity per pack
  45Ah (per cell) x 360.6 V = 16 kWh

## Slide 10: Specification Sheet
Customer Requirement | CR met? (✓or X) | Client Acceptable (✓or X)
CR1 - Battery life sufficient for average commuter |  | 
CR2 - Six or more batteries in vehicle | ✓ | ✓
CR3 - Consumer sellable (safe and durable) product | ✓ | ✓
CR4 - Lightweight | ✓ | ✓
CR5 - Cooling system for electric motor |  | 
CR6 - Compatibility with similar vehicle models | ✓ | ✓
Engineering requirement | Target | Tolerance | Measured/ Calculated Value | ER met? (✓or X) | Client Acceptable? (✓or X)
ER1 – Vehicle Range | 100 Miles | >100 |  |  | 
ER2 – Battery Capacity | 10 kWh | >10 | 16 kWh | ✓ | ✓
ER3 – Production Cost | $1,000 | <1,000 | $300 | ✓ | ✓
ER4 – Power Output | 300 hp | +/- 20 hp |  |  | 
ER5 – Torque Output | 250 ft-lbs | +/- 20 ft-lbs |  |  | 
ER6 – Vehicle Weight | 3,000 lbs | + 50 lbs | 2355 lbs | ✓ | ✓
ER7 – Component Cooling | 200 °F | Less Then 200 °F |  |  | 
ER8 – Quantity of Mounts | 5 | Less Then 5 | 4 | ✓ | ✓
Table 3: Spec sheet CR's
Table 4: Spec sheet ER's
Wyatt Watson

## Slide 11: QFD
Figure 6: Quality functional development
Bryce Greenberg

## Slide 12: Gantt Chart – Updated for testing results
Figure 7 and 8: Gantt chart and current testing progress
Bryce Greenberg