## Slide 1: Formula SAE Suspension
Parker Johnson: Suspension Design Lead
Chris Laney: Brakes Engineer
Garrett Pearson: A-Arm Engineer
Mathew Cusson: Steering Engineer
Joseph Ciao: Pushrod Assembly Engineer
Presentation 3
Page 1

## Slide 2: Sub-Team Description
PHOTO
Page 2 - Garrett
Focus is on the vehicles overall suspension system
Design of A-arm, Brakes, Knuckles, Pushrod assembly, Steering, among other systems.
Overall goal: improvement from last year's design mostly in adjustability and overall drivability including ease of steering.
Why is this important: Suspension directly effects the car's handling, stability, and overall safety. It plays a vital role in maximizing tire contact, improving cornering speed, and ensuring driver control.
Fig. 1: Picture of 1st year Front Suspension System

## Slide 3: Design Requirements (QFD)
PHOTO
Page 3 - Parker
Figure 2. QFD

## Slide 4: Design Description
PHOTO
Page 3 - Parker
The figures above and on the next page shows accurately what our suspension will look like.
Currently the A-arms and the knuckle/brakes assembly are shown, however this will be very useful for a motion study and making sure no moving parts collide throughout its 3” range of travel.

## Slide 5: Design Description
PHOTO
Page 3 - Parker
The above figures show that no parts interfere with the tire/wheel selection our team is going with for our design. (OZ racing 13” and 20.5” Hoosier Tires)

## Slide 6: Design Description – Knuckles
LL
Page 4 - Parker
The Knuckle connects the wheel to all other suspension components such as the A-arms, brakes, and steering
Defines steering geometry
Must be strong enough to withstand many forces simultaneously
Figure 3. Knuckle Assembly Drawing

## Slide 7: Design Description – Knuckles
LL
Page 5 - Parker
General steering knuckle design
3 step manufacturing process
Features a press fit tolerance for the wheel bearing, and snap ring groove
Aluminum for easy machinability and weight
Figure 4. Knuckle parts drawing

## Slide 8: Design Description – Knuckles
LL
Page 6 - Parker
Figure 5. Knuckle parts part 2

## Slide 9: Design Description – Pushrod
LL
Page 7 - Joe
Figure 6. Rocker Arm Version 1
Figure 7. Pushrod
Figure 8. DHx2 Damper

## Slide 10: Design Description – Pushrod
LL
Page 8 - Joe
Rocker arm will rotate up and down to compress or decompress springs
Rocker dimensions:
3.5 in x 2.5 in x 4.17 in
This gives a motion ration 1.5
To make Manufacuring easier rocker is all one thickness at .4 in and more material was removed to keep weight low
Rocker arm must be able to sustain 3500 N of force.
Figure 9. Rocker Arm Assembly Drawing

## Slide 11: Design Description - Steering
LL
Page 9 - Matt
Tie Rod system is what connects the steering rack to the knuckle
Tie rod tube hollow for weight reduction
Threaded insert to hold rod end
Rod ends for adjustability
Jam nut for locking
Operational order -
Driver turns wheel
Wheel turns steering column
Steering column turns rack
Rack moves knuckle laterally
Knuckle changes wheel angle
Figure 10. Tie Rid Drawing

## Slide 12: Design Description – Control Arms
LL
Page 10 - Garrett
Figure 11. Front Left Lower Control Arm
Figure 12. 5/16 Rod End
Figure 13. ½” Spherical Bearing

## Slide 13: Design Description – Control Arms
LL
Page 11- Garrett
Figure 14. Control Arm Part List Drawing

## Slide 14: Design Description - Brakes
LL
Page 12 - Chris
Design Features:
Adjustable pedal ratio
Sliding rail mount for position adjustment
Balance bar for brake bias tuning
~¾" adjustment on threads
Operation order:
Driver presses brake pedal with adequate force
Master cylinders are compressed, with a certain percentage going to the front MC and some going to the rear depending on the bias bar
Fluid is forced through the MC and then through the brake lines
Brake pads are compressed evenly on rotor
Figure 15. Brake Pedal assembly

## Slide 15: Design Description - Brakes
LL
Page 13 - Chris
Figure 16. Brake Pedal Box Drawing

## Slide 16: Design Description - Brakes
LL
Page 13 - Chris
Figure 16. Brake assembly

## Slide 17: Design Description - Brakes
LL
Page 13 - Chris
Figure 16. Brake assembly Drawing

## Slide 18: Engineering Calculations- Pushrod
LL
Page 14 - Joe
Initial Solidworks stress test showed the current design holds up well to the current max force(3500 N). Now last tests will be performed in Ansys to finalize design.
Variables:
Pcr = Critical Load
E = Young's modulus of pushrod material
(aluminum 10*106 psi)
I = Aera moment of inertia of pushrod cross-section
L = Length of pushrod
(22.1 in*this will change)
K = Column effective length factor
(1.0)
Buckling Calculation:
Pcr=(πEI)/(KL)2
I =(π(.25 in)4)/4= .00307 in4​
Pcr= (π2*(10*106 psi ) * .00307 in4)/(1.0*22.1 in)2= 620.4 Ibf
Figure 17. Rocker Arm Stress results
Figure 18. Pushrod stress results

## Slide 19: Engineering Calculations-Geometry
LL
Page 15 - Parker
Created matlab code using suspension geometry in CAD to model forces in the pushrod system
Used worse case loading scenario to acquire a minimum value of 700 lbf/in spring rate
Since the loading scenario is unrealistic for application, we will try a few spring rates of 400 and 500 lbf/in
This will give us more desirable values for down travel for better handling over bumps

## Slide 20: Engineering Calculations-Geometry
LL
Page 16 - Parker
Used worse case scenario forces to model a FBD to determine the loads on the control arms
Values of 4000 N vertically and 2400 N horizontally were determined for the force acting on the center of tire contact patch.
1400 N (tension) for upper control arms and around 4000 N in compression for the lowers
These values will be used for ANSYS analysis on control arms and will help with ANSYS on the steering knuckles

## Slide 21: Engineering Calculations-Steering
LL
Page 17 - Matt
Figure 19. - Steering Geometry
For calculations I use base tie rod lengths
11.4 in
17.4 in
14.4 in
These are based on NARRCO steering rack length and the tie rods needed for using them
Values for bump and droop -
11.4: bump .85 deg droop .16 deg
14.4: bump .24 deg droop -.12 deg
17.4: bump .30 deg droop .05 deg
Values show desirable results to continue using 14.4 inch rack

## Slide 22: Engineering Calculations – Control Arms
LL
Page 18 - Garrett
Figure 20. Control Arm Force

## Slide 23: Engineering Calculations- Brakes
LL
Page 19 - Chris
Calculating the Lock-Up Force(Front axle)
Dynamic on Front Axle = Mass*(Lr+h)/L = 78% percent front, 22% rear
Longitudinal load Transfer (Ft) = µ*m*h*g/L = 1399 N
Normal Force on Front Tyres (Fnf) = ((m*g*Lr)/L) +Ft = 2098 N
Lock-Up Force(Ff) = Fnf** µ/2 = 1468 N
Lock-Up Torque = Ff*R = 391 N/m
391 = (2)(0.5)(Brake Line Pressure)(piston area)(average effective radius)
Lock-Up Brake Line Pressure = 5.83 e 6 N/m^2 = ~750 psi
With 5/8" bore master cylinders front and rear, this equates to 400N input force at the pedal
Figure 21. MATLAB code for brakes

## Slide 24: FMEA chart
LL
Page 20 - Parker

## Slide 25: Testing Procedures
LL
Page 21 - Parker
Our goal is to test the car several times, one of the times being on campus in the space provided to us by parking services.
All day event, consisting of several testing procedures of the vehicle handling, steering force required, braking distances, and measuring tire temps to adjust static camber.
The spring rate will also be tested and we will decide how to adjust based off handling characteristics.
Iterative testing will be done to test the heat capacities of components along with their wear rates
We will need ample space, volunteers, safety equipment, tools, replacement parts and other parts for changing geometry
We will also be doing an additional testing day will the 3 other state universities

## Slide 26: Schedule and Budget
LL
Page 22 - Parker

## Slide 27: Next Steps
LL
Page 23 - Parker
Do a full assembly with motion analysis, confirming our design will work as intended.
Finalize forces acting on all components, bring to ANSYS and do any necessary design adjustments.
Update full assembly and confirm parts will still work
Finalize manufacturing processes and order stock, parts, hardware and all materials

## Slide 28: Thank you!