## Slide 1: Boeing Autonomous Driving
Elise C., Selina C., Jacob K., Marek L., Desirae M., Natasa P., Lily Q.

## Slide 2: Project Description
Control system to Automate Traditional Vehicles
  Brakes
  Steering
  Throttle
Sponsors and Stakeholders
  Boeing (Michael Vogelsang)
  Technical Support (Conner N. and Donald G.)
Importance
  Future Transportation
  Advanced Automation Technology
SC 2
Vehicle of Our Choice [1]

## Slide 3: Black Box Model
Drive
Autonomously
Sensors
Speed
Wheel Direction
Acceleration
Wheel Turning
Decisions
Cameras and Lidar
Speedometer
Gyroscope
ML 3

## Slide 4: Functional Decomposition
JK 4

## Slide 5: Brakes Functional Decomposition Chart
JK 5

## Slide 6: Steering Functional Decomposition Chart
DM 6

## Slide 7: Throttle Functional Decomposition Chart
NP 7

## Slide 8: Brakes Concept Generation
JK 8
Sketch/Design 1: Autonomous Braking System
Bolt in Bracket
Mechanical Arm
Motor Shaft
Motor
Design Considerations | Performance Targets
Evaluated: Hydraulic and electro-hydraulic Systems. | Achieve: 500ms response time
Explored: Dual-mode (autonomous/manual) design. | Ensure 10-hour operational reliability.
Design Considerations | Performance Targets
Explored: Hydraulic motor integration with motor attachment | Achieve: 1800 RPM for 2.68 MPa pressure output
Evaluated: Solenoid valve diverter for fluid flow control | Ensure: On/Off Capabilities
Design 2: Brake Booster [2,3,4]
Design Considerations | Performance Targets
Evaluated: H-bridge board for motor communication | Ensure: 1800 RPM for 2.68 MPa output
Assessed: Baseplate for component mounting | Optimize: weight with aluminum
Design 3: Precision Brake Booster [5,6,7]
Hight Torque DC Motor
High-Pressure Hydraulic Pump
Hydraulic Valve Diverter
Solenoid Valve 12V DC
DC H-Board Motor Driver

## Slide 9
Brakes Specifications Chart | Option 1 | Option 2 | Option 3 [8]
Seal Material | Nitrile | Viton (fluorocarbon) or polyurethane | Viton (glycol-ether and borate Resistant)
Max Pressure | 2500PSi | 3000PSI | 725 PSi
Max Flow Capacity | 0.82 | 0.95 | .013
Electrical Connectivity | N/A | 12V DC ; 1.7Amps (active) | 12V DC ; 1-2Apms (active)
Total Price | $80 | $110 | $95
Fail-Safe Operation | Manuel On/Off | Electrically Switched On/Off | Electrically Switched On/Off
Brakes Specifications Chart | Option 1 | Option 2 | Option 3 [8]
Seal Material | Nitrile | Viton (fluorocarbon) or polyurethane | Viton (glycol-ether and borate Resistant)
Max Pressure | 2500PSi | 3000PSI | 725 PSi
Max Flow Capacity |  |  | 
Electrical Connectivity | N/A | 12V DC ; 1.7Amps (active) | 12V DC ; 1-2Apms (active)
Total Price | $80 | $110 | $95
Fail-Safe Operation | Manuel On/Off | Electrically Switched On/Off | Electrically Switched On/Off
JK 9

## Slide 10
Brakes Option Comparison | Concept 1 | Concept 2 | Concept 3
Advantages | Simple, direct interface (pedal push) Uses existing hydraulics Low electronics requirement Intuitive fail-safe Lower complexity | Automated actuation with fluid pump On/off solenoid provides simple pressure modulation | Precise control with Raspberry Pi + stepper/driver Hydraulic isolation Autonomous flexibility Layered safety
Disadvantages | Size Cost | More components Solenoid only allows binary (on/off) control | Requires advanced tuning (H-bridge to motor control) More failure points (electronics + hydraulics)
JK 10

## Slide 11: Steering Concept Generation
DM 11
Sketch: Autonomous Steering System
Steering Wheel
Moving Mechanism that will control steering
Pinion
Rack
Design Considerations | Performance Targets
Evaluated: | Achieve: 500ms response time
Explored: Autonomous & Manual Design | Ensure: User Interference
Design Considerations | Performance Targets
Explored: Servo Motor with a servo controller or DIY servo-motor with a normal brushless motor | Achieve: Steering subsystem to connect to electrical "hivemind"
Evaluated: Cost, weight, and reliability | Ensure: Killswitch Capabilities
Potential Components of Steering System [9,10]
Design Considerations | Performance Targets
Evaluated: Hydraulic, electric, and DIY electric steering kits | Ensure: Functions autonomously
Assessed: Cost, potential steering options, weight | Optimize: Reliability, Modification-ability, Cost, Complexity
Our Options [11,12]
Servo Motor
Servo Controller

## Slide 12
SC 12
Steering Specifications Chart | Option 1: Electric Power Steering (EPS) Kit [11] | Option 2: Hydraulic Power Steering (HPS) Kit [S2] | Option 3: DIY EPS Kit
Motor | Pre-installed DC Motor | Hydraulic Pump | DC Motor (User-Chosen)
Power Source | 12V/24V Battery | Hydraulic Fluid Pump | 12V/24V Battery
Steering Mechanism | Rack-assist | Welded Hydraulic Cylinders | Custom Rack & Pinion
Torque Sensing | Torsion Bar & a Sensor | Torsion Bar & a Rotary Valve | Torsion Bar & a Sensor
Position/Angle Steering | Rotary Encoder on Column | Column Angle Potentiometer | Encoder/Sensor (User Chosen)
Failsafe | Killswitch | Mechanical Lockout | Killswitch

## Slide 13
Steering Option Comparison | Option 1: Electric Power Steering (EPS) Kit [11] | Option 2: Hydraulic Power Steering (HPS) Kit [12] | Option 3: DIY EPS Kit
Advantages | Better Fuel Efficiency Lower Emissions Lighter Weight Fewer Components Power-On-Demand | Provides High Power to Weight Ratio Flexible Energy Transfer Precise Control Over Speed & Force Less Costly to Repair | Inexpensive Modifiable Customized Specs More informed about the system
Disadvantages | Reduced Road Feel High Repair Costs Expensive (~$600-$1000) Environmental Impact from Materials | Maintenance Requirements for Leaks Noise Lower Efficiency Fire Hazard (flammable fluids) | Time Consuming Research Heavy Prototyping
LQ 13

## Slide 14: Throttle Concept Generation
Design Considerations | Performance Targets
Evaluated: | Achieve: 0.5 s Response TIme
Explored: Autonomous vs. Manual Throttle | Ensure: User Override
Design Considerations | Performance Targets
Explored: Rotary Servo actuator with Connected Potentiometer or Built-In Linear Actuator | Achieve: Throttle Subsystem with Predictive Acceleration Control
Evaluated: Power, Cost, and Mounting Location | Ensure: Kill Switch or Limit Switches
Design Considerations | Performance Targets
Evaluated: Rotary Servo, linear actuator, and stepper motor | Ensure: Functions autonomously
Assessed: cost, ease of integration | Optimize: Reliability,
Our Options
NP 14
Gearbox
Potentiometer
Picture: Go-Kart Drive By Wire System
Possible Throttle Components
Drive-By-Wire
[13]

## Slide 15
Throttle Specifications Chart | Option 1: Rotary Servo + Potentiometer | Option 2: Linear Actuator | Option 3: Stepper Motor
Torque at Max Load | 2.9 Nm | 3 Nm (0.01 m lever arm) | 2.4 Nm
Assembly | Throttle Lever via Rotary Linkage | Throttle Lever via Linear Linkage | Throttle Lever via Linkage/Gear
Sensor Connectivity | LMC13 Linear Motion Potentiometer | Built-In Linear Potentiometer with Position Feedback | Requires Potentiometer or Encoder
Stroke Distance (mm) | 11mm (Potentiometer) | 100 mm | N/A
Total Price | $165.70 | $90 | $18.92
Safety | Added E-Stop | Limit Switches & E-Stop | Added E-Stop
NP 15
[14] [15]
[16]
[17]

## Slide 16
Throttle Option Comparison | Option 1: Servo + Potentiometer | Option 2: Linear Actuator | Option 3: Stepper Motor + Potentiometer
Advantages | Close-Loop Control High accuracy (± 0.25°) Consistent torque High efficiency Rapid acceleration | Close-Loop Control Precise control (± 0.5 mm) Self-locking ability Simple design Potentiometer integrated | Potentiometer or Encoder Necessary for Close-Loop Greater Torque Cheaper Reliable
Disadvantages | Higher cost Complex controller Overload Susceptibility Potential for unpredictability | High cost Limited force | Low efficiency Noise & vibration Not Accurate for (extremely) high speeds
NP 16
[14] [15]
[16]
[17]

## Slide 17: Morphological Matrix - Brakes
Options | 1 | 2 | 3
Power Source | 24V | 24V | 24V
Control Mechanism | Push Rod | 24V DC Motor [5] | H-Board [7]
Actuation Method | 24V DC Motor | On/Off Solenoid (Manuel) [4] | On/Off Solenoid Electric [8]
Feedback Mechanism | N/A | N/A | Raspberry-pi [18]
Safety Features | On/Off | On/Off Solenoid & Manuel | On/Off Solenoid Electric & Motor On/Off Electric & Manuel
JK 17

## Slide 18
Morphological Matrix - Steering
Options | 1 | 2 | 3
Power Source | 12V-24V | Hydraulic Fluid Pump | 12V-24V
Control Mechanism | ECU [19] | Motor Controller [20] | Servo Controller [10]
Actuation Method | DC Motor [21] | Hydraulic Pump [22] | Servo Motor [9]
Feedback Mechanism | Current Sensor [23] | Torsion Bar & A Rotary Valve [24] | Potentiometer [25]
Safety Features | Safe fallback mode | Engine Shut off | DIY Kill Switch
SC 18

## Slide 19
Morphological Matrix - Throttle
Options | 1 | 2 | 3
Power Source | 12V Battery | 24V Battery | 12V Battery
Control Mechanism | H-Bridge Board [26] | Raspberry Pi [27] | Arduino Nano [28]
Actuation Method | Rotary Actuator | Linear Actuator | Stepper Motor
Feedback Mechanism | Potentiometer | Built-In Potentiometer | Rotary Encoder [29]
Safety Features | High-Power Killswitch [30] | Limit Switch [31] | Lower-Power Killswitch [32]
NP 19

## Slide 20: Brakes: Pressure Generated By Petal Force
Equations [33,34,35]
= ()
= ()
Goal: Determine the master cylinder pressure (Pa) produced by a given pedal force (N) and quantify how variations in pedal input affect the resulting braking pressure
Variables & Visual | 
(Pedal Force)= | 
 | (Pedal length)
(Input rod dist. from fulcrum) = 0.0508 m | (Master Cylinder Diameter) = 0.0159 m
(Master Cylinder Pressure)= | 
Variables & Visual | 
Solutions
= 63.04 N
= 318 Pa
JK 20
Moving Forward: Compare estimated data with measured values after the buggy is assembled and refine calculations for accuracy.

## Slide 21: Brakes: Time and Distance to Stop
Equations [36,37]
ML 21
Solutions
Goal: Estimate the total distance and time it takes to bring the kart to a full stop from our maximum speed given by our client.
Moving Forward: This estimation shows that if we want to improve our time and distance to stop that we will need to decrease our reaction time as well as include a deceleration coefficient once we have our cart measurements to have closer estimates.
Variable | Value
v = Starting Velocity | 9 (m/s)
= Reaction time | .5 (s)
= Friction Coefficient | .7
= Gravity | 9.81
a = Acceleration | 6.87
Variable | Value
v = Starting Velocity | 9 (m/s)
 | .5 (s)
 | .7
a = Acceleration | 

## Slide 22: Steering: Minimum EPS Kit Motor Power
Goal: Determine the minimum motor power needed for an electric power steering system, considering a gear train between the motor and the steering rod.
Moving Forward: We should look for or make an electrical power steering kit with a minimum motor power of 307.2W. This is reasonable because a typical EPS kit found online provides 200W-600W.
SC 22
Variables | Values
Front Axle Load Fraction () | 40% [42]
Total Mass (Go-Kart + Driver) | 200kg
Velocity ( | 6 m/s
Minimum Turning Radius | 3.5 meters [1]
Gear Ratio (GR) | 2
Gear Efficiency() | 0.9
Average Ackermann Angle () | 0.336 rads [43]
Manuver Time () | 0.5 seconds
Variables | Values
 | 40% [42]
Total Mass (Go-Kart + Driver) | 200kg
 | 6 m/s
Minimum Turning Radius | 3.5 meters [1]
Gear Ratio (GR) | 2
 | 0.9
 | 0.336 rads [43]
 | 0.5 seconds
Equations [38,39,40,41]
Solutions

## Slide 23: Steering: Motor torque & Gearbox Ratio Selection
Goal: Determine gearbox ratio G and motor torque to deliver the torque assist
Moving Forward: A 1.0Nm motor with a 45:1 gearbox provides about 40Nm at the shaft and meets the assist target
DM 23
Variables | Values
Estimated maximum required torque at steering shaft () | 
Motor Torque () | 
Desired assist fraction (a) | 100%
Gear Efficiency () | 0.9
Variables | Values
Desired assist fraction (a) | 100%
 | 0.9
Equations
[44]
[44]
Solutions

## Slide 24: Throttle Calculation – Linear Force
Goal: Calculate the force the actuator must apply onto the pedal to achieve a 2.5 N force for full throttle. Analyze how this force changes with varying lever arm distances.
Linear Actuator
At At
Moving Forward: This helps decided where to place the actuator
EC 24
Variable | Value
- desired pedal force | 2.5 N
- Pedal pad distance from pivot | 0.30 m
- Lever arm length where actuator attaches | 
FS - factor of safety | 2
Variable | Value
 | 2.5 N
 | 0.30 m
FS - factor of safety | 2
Notes: Fail-safe (return spring) is easy to implement because actuator pushes/pulls directly on the pedal. A linear actuator can directly replicate the pulling/pushing motion of the throttle cable → no need to carefully design extra linkages.
A servo or stepper motor produces torque (rotational force). To use them, you’d need to design a linkage or gear system to translate that torque into a push/pull motion on the carburetor arm.
This makes a linear actuator simpler, more direct, and easier to size because you only need linear force, not torque conversion.

## Slide 25: Throttle Calculation – Linear Speed
Goal: Determine the highest linear speed the actuator can achieve based on the different mounting radius using a linear force of 30N.
Equations:
    T = F x r
Constraint: Actuator limited to 4 mm/s
Moving Forward: The team must consider 0.04m mounting radius to offer the highest linear speed of the actuator without exceed its mechanical limits. This will also be useful in determining potential conflict with brake mechanism.
NP 25
Variable | Value
, linear displacement of actuator ( | 0.1
, stroke angle () | 3.33
, desired response time () | 0.5
, output angular velocity (rpm) | 1.11
, screw lead in linear actuator | 1
G, gear ratio | 256:1
Variable | Value
 | 0.1
 | 3.33
 | 0.5
 | 1.11
 | 1
G, gear ratio | 256:1
  Solutions:
    Iteration 1:
      r = 0.02m
      v = 2.32 mm/s
      T = 0.6 Nm
    Iteration 2:
      r = 0.04m
      v = 4.65 mm/s
      T = 1.2 Nm
    Iteration 3:
      r = 0.06m
      v = 6.97 mm/s
      T = 1.8 Nm
[45]

## Slide 26: Brakes Concept Evaluation – Pugh Chart
ML 26
Criteria | Design 1 – Booster with Solanoid | Design 2 - Booster | Design 3 – Pedal Actuator
Speed | D A T U M | s | -
Reliability |  | s | s
Cost |  | s | +
User Interference |  | s | -
Ease of Installation |  | s | +
Electrical Integration |  | - | -
Total: |  | -1 | -1

## Slide 27: Brakes Concept Evaluation – Decision Matrix
ML 27
Criteria (Out of 5) | Weight | Design 1 – Booster with Solanoid |  | Design 2 - Booster |  | Design 3 – Pedal Actuator | 
 |  | Unweighted Score: | Weighed Score: | Unweighted Score: | Weighed Score: | Unweighted Score: | Weighed Score:
Speed | 25% | 100 | 25 | 100 | 25 | 60 | 15
Reliability | 20% | 100 | 20 | 100 | 20 | 40 | 8
Cost | 15% | 20 | 3 | 40 | 6 | 60 | 9
User Interference | 20% | 100 | 20 | 100 | 20 | 20 | 8
Ease of Installation | 5% | 20 | 1 | 40 | 2 | 60 | 3
Electrical Integration | 15% | 100 | 15 | 60 | 9 | 20 | 3
Total: | 100% | Sum: | 84 | Sum: | 82 | Sum: | 46

## Slide 28: Concept Selection – Booster with Solenoid
ML 28
Pros
Better reaction times
No Interference with User-Controlled Modes
Easy to Capture Measurements and Electrical Integration
Cons
Expensive
Invasive

## Slide 29: Concept Selection – Booster with Solenoid
ML 29
8”
6”
Simple Base Plate Design with Cost Analysis

## Slide 30: Steering Concept Evaluation- Pugh Charts
LQ 30
Criteria | Electric Power Steering (EPS) Kit | Hydraulic Power Steering (HPS) Kit | DIY EPS Kit
Customizability | D A T U M | - | +
Mass Weight |  | - | s
Complexity of Integration |  | - | -
Cost |  | s | +
Maneuverability |  | - | s
User Interference |  | + | s
Total |  | -3 | +1

## Slide 31: Steering Concept Evaluation- Decision Matrix
Criterion | Weight | Electric Power Steering (EPS) Kit |  | Hydraulic Power Steering (HPS) Kit |  | DIY EPS Kit | 
 |  | Unweighted Score | Weighted Score | Unweighted Score | Weighted Score | Unweighted Score | Weighted Score
Customizability | 20% | 50 | 10 | 30 | 6 | 100 | 20
Mass Weight | 20% | 100 | 20 | 70 | 14 | 80 | 16
Complexity of Integration | 10% | 80 | 8 | 60 | 6 | 50 | 5
Cost | 20% | 50 | 10 | 60 | 12 | 90 | 18
Maneuverability | 10% | 90 | 9 | 80 | 8 | 80 | 8
User Interference | 20% | 90 | 18 | 80 | 16 | 85 | 17
Total | 1 | Sum: | 75 | Sum: | 62 | Sum: | 84
DM 31

## Slide 32: Concept Selection – DIY EPS Kit
Chosen Concept: DIY EPS Kit
Pros
  Budget Friendly
  Customizable
  Hands on expertise
Cons
  Time consuming
  Research Heavy
Rough CAD for Gear Assembly
SC 32

## Slide 33: Concept Selection – DIY EPS Kit
Dimensions of Gear
Testing Assembly with FEA
SC 33

## Slide 34: Throttle Concept Evaluation - Pugh Chart
EC 34
Criteria | Servo + Potentiometer | Linear Actuator | Stepper Motor + Potentiometer
Reliability | 0 | D A T U M | -
Cost | - |  | +
Ease of Integration | - |  | -
Response Time | + |  | +
Efficiency | + |  | -
Power Consumption | - |  | 0
Total | -1 |  | -1

## Slide 35: Throttle Concept Evaluation – Decision Matrix
Criteria | Weight | Servo + Potentiometer |  | Linear Actuator |  | Stepper Motor + Potentiometer | 
 |  | Unweighted Score | Weighted Score | Unweighted Score | Weighted Score | Unweighted Score | Weighted Score
Reliability | 25% | 80 | 20 | 100 | 25 | 60 | 15
Cost | 15% | 20 | 3 | 60 | 9 | 100 | 15
Ease of Integration | 15% | 40 | 6 | 100 | 15 | 40 | 6
Response time | 25% | 100 | 25 | 80 | 20 | 60 | 15
Efficiency | 10% | 100 | 10 | 100 | 10 | 0 | 0
Power Consumption | 10% | 0 | 0 | 80 | 8 | 80 | 8
Total | 100% | Sum: | 64 | Sum: | 87 | Sum: | 59
EC 35

## Slide 36: Concept Selection – Linear Actuator
Pros
  Simple Electrical Integration
  Built-in Potentiometer
  Linear Mechanism
Cons
  Higher Price
  Force Limited
EC 36
Imported CAD of Linear Actuator [3]

## Slide 37: Concept Selection – Linear Actuator
Dimensions of Simulated Spring
FEA Strain Test on Spring
NP 37
Notes: This is a simulated estimation of the spring inside of the actuator. We plan to do more testing when we receive the go kart and actuator

## Slide 38: Gantt Chart - Brakes
ML 38
Steering Subsystem | Start Date | End Date | Estimated Hours | Hours Spent | WK4 | WK5 | WK6 | WK7 | WK8 | WK9 | WK10 | WK11 | WK12 | WK13 | WK14
Measurements of Vehicle and Research | 14-Sep | 28-Sep | 14 | 16 |  |  |  |  |  |  |  |  |  |  | 
Decide Design for Braking | 21-Sep | 28-Sep | 7 | 7 |  |  |  |  |  |  |  |  |  |  | 
Protoype 1 | 22-Sep | 20-Oct | 28 | 10* |  |  |  |  |  |  |  |  |  |  | 
Prototype 2 | 21-Oct | 10-Nov | 20 | - |  |  |  |  |  |  |  |  |  |  | 
Integration with Sensors | 1-Nov | 1-Dec | 30 | - |  |  |  |  |  |  |  |  |  |  | 
Prototype 3 | 11-Nov | 1-Dec | 20 | - |  |  |  |  |  |  |  |  |  |  | 

## Slide 39: Gantt Chart - Steering
Steering Subsystem | Start Date | End Date | Estimated Hours | Hours Spent | WK4 | WK5 | WK6 | WK7 | WK8 | WK9 | WK10 | WK11 | WK12 | WK13 | WK14
Research Options | 15-Sep | 25-Sep | 10 | 10 |  |  |  |  |  |  |  |  |  |  | 
Begin Drafting Designs | 26-Sep | 6-Oct | 10 | 15 |  |  |  |  |  |  |  |  |  |  | 
Budget & Purchase Materials | 7-Oct | 14-Oct | 7 |  |  |  |  |  |  |  |  |  |  |  | 
Prototype 1 | 15-Oct | 30-Oct | 15 |  |  |  |  |  |  |  |  |  |  |  | 
Prototype 2 | 31-Oct | 15-Nov | 15 |  |  |  |  |  |  |  |  |  |  |  | 
Prototype 3 | 16-Nov | 1-Dec | 15 |  |  |  |  |  |  |  |  |  |  |  | 
LQ 39
Notes: Whoever is presenting this, announce "We are on track, but a little behind with drafting designs."

## Slide 40: Gantt Chart - Throttle
EC 40

## Slide 41: BOM - Brakes
ML 41
Brake System Requirements |  |  |  |  |  | 
BoM Level | Part # | Description | Qty | Units | Unit Cost | Total Cost
5 | XD-3420 | 12V Motor | 1 | 1 | $23.60 | $23.60
4 | JFHSV0003 | High Pressure Solenoid Valve | 1 | 1 | $85.00 | $85.00
4 | Oukan78 | Hydraulic Pump | 1 | 1 | $45.21 | $45.21
4 | BTS7960B | H-Board | 1 | 1 | $86.99 | $86.99
4 | 01 | Base Plate (Mounting) | 1 | 2 | $5.78 | $11.56
Total Number of Parts |  |  | 5 | Total Costs |  | $225.36

## Slide 42: BOM - Steering
DM 42
Steering System Requirements |  |  |  |  |  | 
BoM Level | Part # | Description | Qty | Units | Unit Cost | Total Cost
2 | Q830 | Pinion | 1 | 1 | $23.70 | $23.70
2 | 3100A0 | Gear | 1 | 1 | $71.09 | $71.09
3 | 519-CEP2223S | Motor | 1 | 1 | $59.95 | $59.95
3 | 1PZT40-SA1 | Torque Sensor | 1 | 1 | $14.59 | $14.59
3 | HW | Mounting Hardware | 4+ | 8 |  | 
3 | RASP-PI | Microcontroller (i.e., Arduino Raspberry Pi) | 1 | 1 | $86.99 | $86.99
4 | FB | Wiring Harness (Feedback) | 1 | 2 | $3.99 | $7.98
Total Number of Parts |  |  | 10 | Total Costs |  | $267.30

## Slide 43: BOM - Throttle
NP 43
Throttle Actuation System Requirements |  |  |  |  |  | 
BoM Level | Part # | Description | Qty | Units | Unit Cost | Total Cost
1 |  | Actuation System |  |  |  | 
2 | P16-P | Linear Actuator with Feedback | 1 | 1 | $90.00 | $90.00
2 | TL-LK | Throttle Linkage ( i.e., Clevis and Bracket) | 2+ | 4 | $2.99 | $11.96
2 |  | Electronics |  |  |  | 
3 | RS-01 | Return Spring (Failsafe) | 1 | 1 | $7.99 | $7.99
3 | FUSE-7A | Fuse | 1 | 1 | $5.95 | $5.95
3 | HB-5A | H-Bridge | 1 | 1 | $6.99 | $6.99
3 | HW | Mounting Hardware | 4+ | 8 |  | 
3 | RASP-PI | Microcontroller (i.e., Arduino Raspberry Pi) | 1 | 1 | $86.99 | $86.99
4 | FB | Wiring (Feedback) | 1 | 2 | 3.99 | $7.98
Total Number of Parts |  |  | 12 | Total Costs |  | $217.86

## Slide 44: Budget
EC 44
Category | Description | Amount ($)
Boeing Funding | One-time contribution | 5,000.00
Fundraising | Ongoing donations/sponsorships | 0.00
Go Kart |  | 1,746.00
Fire Extinguishers | Safety equipment | 37.78
Custom Domain | Website | 17.18
Total Income (Current) |  | 5,000.00
Total Expenses (Current) |  | 1,800.96
What’s Left Over (Current) |  | 3,199.04
SUBTEAM | ESTIMATED BUDGET ($) | NOTES
Brakes | 800 | Motor, Solenoid, Wiring, and Sensors
Steering | 1,000 | Gears, motor, ECU
Throttle | 600 | Actuator, linkage, mounting, electronics
Electrical | 1,625 | Sensors, controllers, wiring, safety shutdown
Travel | 450 | Gas, trailer, van, food
Go Kart | 1,746 | Already purchased
Miscellaneous | 500 | Unplanned materials, tools
Total Estimated Expenses | ~6,721 | 
Notes: Green income red expenses

## Slide 45: Fundraising Update
New Goal of $2,000+
Promoting Awareness:
  Active social media engagement
Fundraising ideas:
  Restaurant percentage night (Chipotle, Raising Cane's)
  3D printing items with logo
  Crochet items
  Bake Sale
  Go Fund Me
DM 45
Example of bake sale set up [47]
Current logo idea [46]

## Slide 46: Electrical Update
Sensors
  Three stereo cameras - primary
  Two LiDAR sensors - redundant
  Inertial Measurement Unit, potentiometers, Load Cell - vehicle state feedback
Software
  Reinforcement Learning System - navigation
  Convolutional Neural Network – dynamic object detection
  Arbitration unit – RL vs CNN
  Raspberry Pi
LQ 46
System Architecture Block Diagram

## Slide 47: Thank you!

## Slide 48: References
[1] “Interceptor XL Mid-size Go Kart, 7hp 4-Stroke Pull Start, Automatic, Full Suspension,” GoKarts USA®, 2024. https://gokartsusa.biz/collections/gokarts/products/gas-mudmonster-212cc-gokart?variant=49825486766396 (accessed Oct. 07, 2025).
[2] Amazon. (n.d.). 12V DC solenoid valve. Retrieved October 7, 2025, from
[3] Temu, "Kuiper Collection: Vintage Decor, Apparel, and Accessories," Temu.com, [Online]. Available: https://www.temu.com/ul/kuiper/un9.html?subj=goods-un&_bg_fs=1&_p_jump_id=894&_x_vst_scene=adg&goods_id=601099770532938&sku_id=17593222883336&adg_ctx=a-630fe82d~c-880e5da2~f-ef23eb73&_x_ads_sub_channel=shopping&_p_rfs=1&_x_ns_prz_type=-1&_x_ns_sku_id=17593222883336&_x_ns_gid=601099770532938&mrk_rec=1&_x_ads_channel=google&_x_gmc_account=5347809690&_x_login_type=Google&_x_ns_gg_lnk_type=adr&_x_ads_account=7917063364&_x_ads_set=22832166925&_x_ads_id=182804198053&_x_ads_creative_id=765792870452&_x_ns_source=g&_x_ns_gclid=EAIaIQobChMI98upjueSkAMVgB1ECB13HSDkEAQYASABEgIEDvD_BwE&_x_ns_placement=&_x_ns_match_type=&_x_ns_ad_position=&_x_ns_product_id=5347809690-17593222883336&_x_ns_target=&_x_ns_devicemodel=&_x_ns_wbraid=CksKCQjw0Y3HBhDLARI6AEuNI-VrswtW06Yyv-aEyhwjryxnhyODqtGsC_ktresuKrWEVQCBv7eBAB-0oyG6tg8OqMj5-OuxghoC8B4&_x_ns_gbraid=0AAAAAo4mICEMi0lT8Cw8ONZlfEQQmG_VS&_x_ns_targetid=pla-2432156726613&gad_source=1&gad_campaignid=22832166925&gbraid=0AAAAAo4mICEMi0lT8Cw8ONZlfEQQmG_VS&gclid=EAIaIQobChMI98upjueSkAMVgB1ECB13HSDkEAQYASABEgIEDvD_BwE. [Accessed: 7 Oct. 2025].
[4] eBay. (n.d.). 12V DC solenoid valve. Retrieved October 7, 2025, from https://ebay.us/m/cn3GSk
[5] HydraForce. (n.d.). HydraForce 12 volt DC NC solenoid valve SV10-22-0-N-00-9-5112-NC. Retrieved October 7, 2025, from https://www.surpluscenter.com/Brands/Hydraforce/Hydraforce-12-Volt-DC-NC-Solenoid-Valve-SV10-22-0-N-00-9-5112-NC.axd
[6] eBay. (n.d.). 12V DC solenoid valve. Retrieved October 7, 2025, from https://ebay.us/m/cn3GSk
[7] Amazon, "DEVMO BTS7960B 43A Double DC Stepper Motor Driver Module H-Bridge PWM Smart Car Compatible with Arduino, Raspberry Pi," Amazon.com, [Online]. Available: https://www.amazon.com/DEVMO-BTS7960B-Stepper-H-Bridge-Arduino/dp/B07SZ4T699?adgrpid=177218412183&hvpone=&hvptwo=&hvadid=748029726649&hvpos=&hvnetw=g&hvrand=15004738281654529711&hvqmt=&hvdev=c&hvdvcmdl=&hvlocint=&hvlocphy=1013462&hvtargid=dsa-2418061332904&hydadcr=&mcid=&hvocijid=15004738281654529711--&hvexpln=67&tag=googhydr-20&hvsb=Computers_d&hvcampaign=dsadesk. [Accessed: Oct. 7, 2025].
[8] U.S. Solid. (n.d.). High pressure solenoid valve - 3/4” 12V DC brass 50 bar, 300°F high-pressure high-temperature solenoid valve. Retrieved October 7, 2025, from https://ussolid.com/products/high-pressure-solenoid-valve-3-4-12v-dc-brass-50-bar-300-high-pressure-high-temperature-solenoid-valve-html
[9] “Ac Servo Motor,” indiamart.com, 2017. https://www.indiamart.com/proddetail/ac-servo-motor-10634229855.html (accessed Oct. 07, 2025).
[10] M. Maestro, “Micro Maestro 6-channel USB,” ServoCity®, 2025. https://www.servocity.com/micro-maestro-6-channel-usb/ (accessed Oct. 07, 2025).
[11] Kit, “Flaming River (FR40200KT): Microsteer Electric Power Steering Kit with Speed Sensor,” Parts Pro News, Apr. 29, 2021. https://partspro.com/blog/flaming-river-fr40200kt-microsteer-electric-power-steering-kit-with-speed-sensor/ (accessed Oct. 07, 2025).
[12] “Full Hydraulic Steering Kit, Most Toyota Truck 4WD PSC Performance Steering Components,” Vividracing.com, 2025. https://www.vividracing.com/full-hydraulic-steering-kit-most-toyota-truck-4wd-psc-performance-steering-components-p-152504776.html (accessed Oct. 07, 2025).

## Slide 49: References
[13] “Reverse Gearbox Kit for Go-Karts with TAV2 Series 30 Torque Converters,” Monster Scooter Parts, 2024. https://monsterscooterparts.com/products/reverse-gearbox-kit-for-go-karts-with-tav2-series-30-torque-converters?srsltid=AfmBOorvc4ThEiKghnmFOR8CgLV_MGSFAYSfSQa2ABHuyGoKIb5yRxij (accessed Oct. 06, 2025).
[14] “Rotary actuators - heavy duty High Torque Gear Motors,” Firgelli Automations, https://www.firgelliauto.com/products/rotary-actuators (accessed Oct. 6, 2025).
[15] “LMC13 series,” P3 America, Inc., https://p3america.com/lmc13-series/?gad_source=1&gad_campaignid=11909418426&gbraid=0AAAAAD_cc-9VsiXAIGU2oTiCopftXqv7L&gclid=CjwKCAjwi4PHBhA-EiwAnjTHuY0I3WLJEMYY5LJTvj7RKkna2yPC5KaE7k0_ejk0cz2QrWyjSsBNTRoCmMIQAvD_BwE (accessed Oct. 6, 2025).
[16] “Actuonix P16-100-256-12-P,” Micro Linear Actuators & Servos - Actuonix Motion Devices, https://www.actuonix.com/p16-100-256-12-p?srsltid=AfmBOoqFERFEDu6hiy8GhymjCY623kLes-Jy3ms5LSeyBhe3DIMiicDL (accessed Oct. 6, 2025).
[17] NEMA 23 Stepper Motor 2.4nm(339.87oz.in) 4A 57x57x82mm 8mm shaft 4 wires - 23hs32-4004s | stepperonline, https://www.omc-stepperonline.com/nema-23-stepper-motor-2-4nm-339-79oz-in-4a-57x57x82mm-8mm-shaft-4-wires-23hs32-4004s (accessed Oct. 6, 2025).
[18] Adafruit Industries, “Raspberry Pi Model 3 A+,” Adafruit.com, 2020. https://www.adafruit.com/product/4027?srsltid=AfmBOorHuoPpt0qwaTCfBDaQneeeOvUpoC3Mu2bjvwnWXNr9S-t4B_VT (accessed Oct. 10, 2025).
[19] “Introduction To Electric Control Unit (ECU): Overview, Types,Components, Communication Protocols And Applications | DIYguru,” DIYguru, Feb. 03, 2025. https://diyguru.org/term/introduction-to-electric-control-unit-ecu/
[20] “Amazon.com: Generic CPC Offroad 200ML Orbital Steering Valve kit with Column and Plate : Automotive,” Amazon.com, 2025. https://www.amazon.com/Generic-Offroad-Orbital-Steering-Column/dp/B0CRCVWKCX (accessed Oct. 10, 2025).
[21] “EPS Steering DC Motor 48V 350W for Forklift Truck,” Made-in-China.com, 2025. https://lifttoppart.en.made-in-china.com/product/ZdLGBFeOwUVt/China-EPS-Steering-DC-Motor-48V-350W-for-Forklift-Truck.html (accessed Oct. 10, 2025).
[22] “LPV - Continental Hydraulics,” Continental Hydraulics, Mar. 03, 2025. https://continentalhydraulics.com/product_items/lpv/ (accessed Oct. 10, 2025).
[23] “ACS712 Current Sensor- 30A,” elecrow.openhardware, Oct. 24, 2013. https://www.elecrow.com/acs712-current-sensor-30a-p-710.html (accessed Oct. 10, 2025).
[24] G. Markel, “Power Steering Repair,” Brake & Front End, May 2005. https://www.brakeandfrontend.com/power-steering-repair/ (accessed Oct. 10, 2025).
[25] Nana and Nana, “Potentiometer for EPS pelletizer machine,” EPSTEC China EPS machine, Nov. 28, 2023. https://www.epstec.com/potentiometer-for-eps-pelletizer-machine/ (accessed Oct. 10, 2025).

## Slide 50: References
[26] “L298N Motor Control Card Dual H-Bridge Module for DC and Stepper Mo...,” Fruugo, 2025. https://www.fruugo.us/l298n-motor-control-card-dual-h-bridge-module-for-dc-and-stepper-motors-2a-output-compatible-with-arduino/p-387982838-832641600?language=en&ac=google&utm_source=organic_shopping&utm_medium=organic (accessed Oct. 10, 2025).
[27] Raspberry Pi Ltd, “Raspberry Pi 5,” Raspberry Pi. https://www.raspberrypi.com/products/raspberry-pi-5/
[28] “Arduino Nano 33 BLE Rev2,” Arduino Online Shop, 2024. https://store-usa.arduino.cc/products/nano-33-ble-rev2?srsltid=AfmBOoqNUel3JqbeXyPycUX_-Ts1sSfs0c50039kNV9bGq75JhG89HrF (accessed Oct. 10, 2025).
[29] “Rotary Encoder - 1024 P/R (Quadrature),” Sparkfun.com, 2023. https://www.sparkfun.com/rotary-encoder-1024-p-r-quadrature.html
[30] Ha, “Royitay Kill Switch for 50cc 70cc 90cc 110cc 125cc 150cc 200cc 250cc ATV Dirt Bike Go Kart Pit Bike 4 Wheeler Quad Trail Bike Ha,” Carkart, 2025. https://carkart.com/products/royitay-kill-switch-for-50cc-70cc-90cc-110cc-125cc-150cc-200cc-250cc-atv-dirt-bike-go-kart-pit-bike-4-wheeler-quad-trail-bike-ha?srsltid=AfmBOop5i9r-PhPLPQBQkJbFkVE1WV1a0MGT6_8XeXEjF60Xo9-zGRWG (accessed Oct. 10, 2025)..
[31] “Welcome To Zscaler Directory Authentication,” Actuonix.com, 2025. https://www.actuonix.com/limit_kit?srsltid=AfmBOoqXyqdP-kfQCTFLkfzyWskN67jnNwFlqkgXJhllUCd7hhTUr7q4 (accessed Oct. 10, 2025).
[32] “PHATMOTO® Rover Kill Switch,” Phatmoto, 2025. https://www.phatmoto.com/products/phatmoto-rover-kill-switch (accessed Oct. 10, 2025).
[33] Fp- . Halliday and R. Resnick, Fundamentals of Physics, 10th ed. Hoboken, NJ: Wiley, 2013.
[34] Ps- J. D. Halderman, Automotive Brake Systems, 7th ed. Boston, MA: Pearson, 2019.
[35] Hammerhead Off-Road, "Mudhead 208R Parts Diagram," Hammerhead Performance, 2022. [Online]. Available: https://hammerheadoffroad.com/pages/parts.
[36] Wikipedia Contributors, “Braking distance,” Wikipedia, Oct. 30, 2019. https://en.wikipedia.org/wiki/Braking_distance
[37] Wikipedia Contributors, “Acceleration,” Wikipedia, Oct. 05, 2025.
[38] “schoolphysics ::Welcome:”:, www.schoolphysics.co.uk. https://www.schoolphysics.co.uk/age14-16/Mechanics/Circular%20motion/text/Centripetal_force_formula/index.html
[39] x-engineer.org, “How to calculate wheel torque from engine torque – x-engineer.org,” x-engineer. https://x-engineer.org/calculate-wheel-torque-engine/
[40] “Angular and Linear Velocity - (Explained with 4 Terrific Examples!),” Calcworkshop. https://calcworkshop.com/radian-measure/angular-and-linear-velocity/

## Slide 51: References
[41] Wikipedia Contributors, “Torque,” Wikipedia, Nov. 01, 2019. https://en.wikipedia.org/wiki/Torque
[42] des dreckett, “How Much Does a Racing Go-Kart Weigh? (UPDATED 2023),” RiiRoo, Aug. 04, 2023. https://riiroo.com/blogs/ride-on-toy-guides/how-much-does-a-racing-go-kart-weigh
[43] J. Vogel, “Tech Explained: Ackermann Steering Geometry,” Racecar Engineering, Apr. 06, 2021. https://www.racecar-engineering.com/articles/tech-explained-ackermann-steering-geometry/[41] R. Budynas, Shigley’s Mechanical Engineering Design ISE. McGraw Hill, 2024.
[44] R. Budynas, Shigley’s Mechanical Engineering Design ISE. McGraw Hill, 2024.
[45] GmbH, R. B. (2014). Automotive Handbook, 9th edition. John Wiley & Sons.
[46] Woloshin, R., Hailey (September, 2025). Autonomous Boeing Draft Logo.
[47] Pinimg.com, 2025. https://i.pinimg.com/originals/9f/1d/21/9f1d214274e08806dd79482ec2d09d4c.jpg (accessed Oct. 09, 2025)