## Slide 1: Boeing Sponsored Retrofitted Go-Kart Designed for Autonomous Driving Boeing Autonomous
Elise C., Selina C., Jake K., Marek L., Desirae M., Natasa P., Lily Q.
Notes: 3 sec

## Slide 2: The Team
Elise Chantegros Budget Liaison
Desirae Mangum Fundraising Lead, Steering Sub-Team Lead
Selina Cozens Steering CAD​​
Jake Keeland
Brakes and Manufacturing
Marek Lemieux
Brake CAD​
Lily Quintanar
Communications Lead​
Natasa Peric Mechanical Engineering Lead, Throttle CAD
NP - 2

## Slide 3: Background
Project Overview
  Control System to Automate Traditional Vehicles​
    Mechanical Focus: Brakes, Steering, Throttle
  Boeing Sponsors: Conner N., Donald G., and Michael V.
  Importance​
    Future Transportation​
    Advanced Automation Technology​
Project Deliverables
  Autonomous Control, Obstacle Detection, User Control, Safety, and Usability
Success Metrics
  Autonomy
    Controlled Turns and Top Speeds
  Reliability
    Fast-Acting Brakes
  Manual Override
  Responsive Feedback
  Kill-Switch
NP - 3

## Slide 4: Design Requirements
Customer Requirements
  Autonomous Navigation
  Obstacle Detection
Engineering Requirements
  User Control
  Performance
  Safety
  Usability
Brakes | Steering | Throttle
ER1 – Manual Override Response Time ER2 – Actuation Response Time ER3 – Brake Disengage Time ER4 – Time to Brake Kart ER5 – Distance Traveled During Braking ER6 – Speed of Actuation ER7 – Maintain User Control ER8 – Speed of Brakes in Rainy Conditions ER9 – Speed of Brakes in Snowy Conditions ER10 – Number of Times Kart can Brake ER11 – 20 min Operation Time ER12 – Intuitive Brake Failsafe Mechanism ER13 – Maintainability of Components ER14 – Protection From Outside Systems | ER1 – Manual Override Response Time ER2 – Actuation Response Time ER3 – Time to Achieve Angle ER4 – Time to Start Turn ER5 – Rate of Steering ER6 – Max Turning Radius ER7 – Left Steering Radius ER8 – Right Steering Radius ER9 – Max Rotation Range ER10 – Left Wheel Angle ER11 – Right Wheel Angle ER12 – Cycles to Failure | ER1 – Max Speed ER2 – Spring Force ER3 – Manual Override Response Time ER4 – Actuation Response Time ER5 – Failsafe Response Time ER6 – Electrical Pedal Force Range ER7 – Throttle Cable Velocity ER8 – Spool RPM at Max Throttle ER9 – Required Force to Pull Throttle
DM - 4

## Slide 5: Houses of Quality
Brakes
Steering
Throttle
DM - 5
Notes: 10 - 20 printed copies

## Slide 6: Design Space Research

## Slide 7: Benchmarking
Tesla
  Navigation
  Heavy Reliance on Camera Detection
Waymo
  Usability
  Challenges to Train LiDAR Cameras
Cruise
  Obstacle Detection
  Currently use LiDAR Control Systems
SC - 7

## Slide 8: Literature Review
Brakes
Fundamentals of Physics, 10th edition [1]
Automotive Brake Systems, 7th edition [2]
On the distribution of braking forces in road braking [3]
Acceleration-deceleration behavior of various vehicle types [4]
Vehicle Braking, Stability and Control [5]
Steering
Reinventing the Wheel: Transforming Steering Wheel Systems for Autonomous Vehicles [6]
Nonlinear Steering Wheel Angle Control Using Self-Aligning Torque with Torque and Angle Sensors for Electrical Power Steering of Lateral Control System in Autonomous Vehicles[7]
Electric Power Steering Automation for Autonomous Driving [8]
Predictive Active Steering Control for Autonomous Vehicle Systems [9]
Automatic Steering System [10]
Throttle
Safety goals and functional safety requirements for actuation systems of automated vehicles [11]
Drive-By-Wire Development Process Based on ROS for an Autonomous Electric Vehicle [12]
NHTSA Rulemakings Related to Automated Driving System-Equipped Vehicles NHTSA Rulemakings Related to Automated Driving System- Equipped Vehicles [13]
Diagnosis of Automotive Electronic Throttle Control Systems [14]
Accurate and Smooth Speed Control for an Autonomous Vehicle [15]
SC - 8

## Slide 9: Mathematical Modeling
Brakes
Estimating Distance Traveled (Marek)
Clamping Force Estimate (Jacob)
Steering
Set Screw Shear Stress Analysis (Selina) [16]
Gear System Stress Analysis (Desirae) [17]
Throttle
Stepper Motor Torque [#]
Bowden Cable Tension [#]
Spring Force [#]
Cable Velocity [#]
SC - 9

## Slide 10: Brakes

## Slide 11: Brakes Functional Decomposition
JK - 11

## Slide 12: Brakes Concept Generation
JK - 12
Sketch/Design 1: Autonomous Braking System
Bolt in Bracket
Mechanical Arm
Motor Shaft
Motor
Design Considerations | Performance Targets
Evaluated: Hydraulic and electro-hydraulic Systems. | Achieve: 500ms response time
Explored: Dual-mode (autonomous/manual) design. | Ensure 10-hour operational reliability.
Design Considerations | Performance Targets
Explored: Hydraulic motor integration with motor attachment | Achieve: 2.68 MPa pressure output
Evaluated: Solenoid valve diverter for fluid flow control | Ensure: On/Off Capabilities
Design 2: Brake Booster
Design Considerations | Performance Targets
Transfer of torque from motor shaft to brake pads | Braking force equal to or greater than the mainline brake system
Baseplate for component mounting | Optimize system such that there are as few points of failure as possible
Design 3: Direct Caliper Actuation System
High-Pressure Hydraulic Pump
Hydraulic Valve Diverter
Docyke Servo Motor
Standard Bicycle Brake Caliper

## Slide 13: Brakes Concept Selection
Pugh Chart
Decision Matrix
Morphological Matrix
Specifications Chart
CAD of Mount Concept
ML - 13

## Slide 14: Brakes FMEA
ML - 14

## Slide 15: Brakes Initial Prototyping
Prototype 1 | Prototype 2 | Prototype 3
Question: How can the motor be mounted? Answer: Opposite side of the mainline caliper as far back on the rear as can fit. Takeaways: Using a spool the mount can be further from the rear | Question: Can the spool design hold up to repeated cycles? Answer: Trading off force needed for speed was too intensive. Takeaways: Remove the spool and directly mount the motor to the caliper | Question: Can we autonomously brake the kart? Answer: Yes. Takeaways: The forces applied to the system are very powerful. A focus on part sustainability was necessary for further testing.
JK - 15

## Slide 16: Brakes Summary
ML - 16

## Slide 17: Brakes Top Level Testing Summary
Experiment/Test | Relevant DRs | Testing Equipment Needed | Other Resources
Motor Test | ER 2 - Actuation Response Time ER 3 - Brake Disengage Time ER 6 - Speed of Actuation | Camera Capable of Slow-Motion Recording Stopwatch Battery Motor PPE Brake Caliper | Personal protective equipment in addition to at least one EE and one EE are required.
Static Brake Test | ER 4 - Time to Brake Kart from Maximum Speed ER 13 - Maintainability of Components | Camera Capable of Slow-Motion Recording Stopwatch Battery Motor PPE Brake Caliper | Personal protective equipment in addition to at least one EE and one EE are required.
Brake Failsafe/Stress Test | ER 1 - Manual Override Response Time ER 7 - Maintaining User Control ER 12 - Intuitive Brake Failsafe | Go-kart Assembled subsystem PPE Battery Failsafe Mounted | Personal protective equipment in addition to at least one EE and one EE are required.
System Limit Test | ER 10 - Number of Brake Cycles from Full Battery ER 11 - 20 Minute Operation Time | Go-kart Assembled subsystem PPE Battery Failsafe Mounted | Personal protective equipment in addition to at least one EE and one EE are required.
Dynamic Brake Test | ER 5 - Distance Traveled while Braking ER 8 - Speed of brake in rainy conditions* ER 9 - Speed of brake in snowy conditions* | Go-kart Assembled subsystem PPE Battery Failsafe Mounted | To properly test ER 8 and 9 we would need the proper weather conditions.
ML - 17

## Slide 18: Brakes Motor Test
Overview: The purpose of this test is to find the time needed to move the motor once given a command, the speed needed to actuate across the needed range of motion, and the time needed to move back from the full state of motion.
Instructions:
1. Complete safety checklist. Secure the cart.
2. Begin recording the system with camera.
3. Provide commands for motor to actuate both directions fully.
4. Measure time for each variable.
5. Repeat across three trials to gather an average.
6. Process data from recording and analyze data for ER specifications.
ML - 18

## Slide 19: Brakes Static Test
Overview: The purpose of this test is to find the time once actuation begins needed to stop the brake given a starting speed equal to or larger than our maximum speed.
Instructions:
1. Complete safety checklist. Secure the cart.
2. Mark a spot on the tire, begin recording and spinning the tire.
3. Provide commands for motor to actuate until at maximum range.
4. Measure speed of tire and time required to stop the tire from beginning of actuation.
5. Repeat across three trials to gather an average.
6. Process data from recording and analyze data for ER specifications.
JK - 19

## Slide 20: Brakes Specification Sheets
Customer Requirement | CR met? (Y or N) | Client Acceptable? (Y or N)
CR1 – Autonomous Navigation | N X | -
CR2 – Obstacle Detection/Avoidance | N X | -
CR3 – Manuel Override | Y ✓ | Y ✓
CR4 – Fail-Safe Design | Y ✓ | -
CR5 – Usability | Y ✓ | -
Engineering Requirements | Target | Tolerance | Measured / Calculated Value | ER met? (✓ or X) | Client Acceptable (✓ or X)
ER1 - Manual Override Response Time | ≤ 500 ms | ±50 ms | 250 ms | ✓ | TBD
ER2 - Actuation Response Time | ≤ 100 ms | ±10 ms | 10 ms | ✓ | TBD
ER3 - Brake Disengage Time | ≤ 100 ms | ±10 ms | 90 ms | ✓ | TBD
ER4 – Time to Brake Kart | ≤ 1000 ms | ±0.100 ms | 830 ms | ✓ | TBD
ER5 - Distance Traveled During Braking (dry) | ≤ 6 m | ±1 m | TBD | TBD | TBD
ER6 - Speed of Actuation | ≤ 100 ms | ±10 ms | 80 ms | ✓ | TBD
ER7 - Ability to maintain user control | Full manual control retained | N/A | TBD | TBD | TBD
ER8 - Braking in Rainy Conditions | Distance increase <50–150% vs dry | Qualitative/TBD | TBD | TBD | TBD
ER9 - Braking in Snowy Conditions | Distance increase <100–200% vs dry | Qualitative/TBD | TBD | TBD | TBD
ER10 - Number of times kart can brake before failure | ≥ 1000 cycles | ±100 cycles | TBD | TBD | TBD
ER11 - Operation Time (continuous) | ≥ 20 min | TBD | TBD | TBD | TBD
ER12 - Intuitive Failsafe Testing | ≥ 90% third-party success | Qualitative | TBD | TBD | TBD
ER13 - Maintainability of Components | Service < 30 min | Qualitative | TBD | TBD | TBD
ER14 - Protection of Subsystem | Weatherproof | Qualitative | TBD | TBD | TBD
JK - 20

## Slide 21: Steering

## Slide 22: Steering Functional Decomposition Chart
LQ - 22

## Slide 23: Steering Concept Generation
Selection Criteria
  Mathematical Conclusions:
    An electrical power steering kit requires a minimum motor power of 307.2W.
    A 1.0Nm motor with a 45:1 gearbox provides about 40Nm at the shaft and meets the assist target.
LQ - 23

## Slide 24: Steering Concept Selection
Pugh Chart
Decision Matrix
Morphological Matrix
Specifications Chart
CAD of Final Concept
LQ - 24

## Slide 25: Steering FMEA
SC - 25

## Slide 26: Steering Initial Prototyping
Prototype 1 | Prototype 2 | Prototype 3
Question: How to mount the motor and electrical components? Answer: 3D Print Mounts Takeaway: Measure components before printing prototypes | Question: How do we align the motor with the steering shaft and prove subsystem feasibility? Answer: 3D-printed gears validate system motion and mounting angle. Takeaway: Pursue manufacturing. | Question: How to manufacture subsystem and include a mechanical failsafe? Answer: Machine with aluminum and use a linear actuator. Takeaway: Machining takes a lot of time and create a cover to protect limit switches.
SC - 26

## Slide 27: Steering Design Summary
SC - 27

## Slide 28: Steering Top Level Testing Summary
Experiment/Test | Relevant DRs | Testing Equipment Needed | Other Sources
Motor Controlled Steering Test | ER6- Left turn radius ER7- Right turn radius | Means to make a video Measuring tape Go Kart | Clear weather Clear course in parking lot Test driver
Time Test 1 (Steering Dynamics) | ER3- Time to Achieve Angle ER4- Time to Start Turn ER5- Rate of Steering | Means to make a video Measuring tape Stopwatch Go Kart | Clear weather Clear course in parking lot No oil/water on roads
Time Test 2 (Override and Safety Response) | ER1- Manual Override Response ER2- Actuation Response Time | Means to make a video Stopwatch Go Kart | Clear weather Clear course in parking lot No oil/water on roads
Steering Rotation and Stress Test | ER8- Max Rotation Range ER9 - Left Wheel Angle ER10 - Right Wheel Angle | Measuring tape Go Kart Means to make a video Means to track cycles Means to mark rotation | Clear weather Clear course in parking lot
DM 28

## Slide 29: Steering Motor Controlled Test
Overview: This test measures the radius required to perform turns with the steering system. The ERs being tested are the left turn radius and right turn radius. This test will verify that these ranges are within safe and operational limits. assessed the system’s ability to had the stress caused by a system endurance test of violently motion of the system for 5 continuous minutes. This showed how the system will react in the even the most unlikely of situations.
Instructions:
1. Complete safety checklist. Secure the cart outside on level ground.
2. Run initial motor test to ensure system behaves as expected before passenger enters.
3. Perform turn test by inputting commands.
4. Measure radius of turn and repeat for other direction.
5. Repeat all measurements for accuracy.
DM - 29

## Slide 30: Steering Rotation Test
Overview: The max rotation angle test will answer what is the full range that the go kart can steer. The rotation test measures the angle required to perform turns with the steering system. The ERs being tested are the left wheel angle, right wheel angle, and max rotation range. These test will verify that these ranges are within safe and operational limits.
Instructions:
1. Complete safety checklist. Secure the cart on level ground.
2. Pull steering wheel to limit on the left.
3. Mark angle of the tire from exterior position of both tires. Repeat on the right.
4. Position angle finder to match up with marks and measure the angle. Repeat measurements for accuracy.
5. Turn the wheels of the kart fully to the left and mark the exterior wheel placement.
6. Turn the wheels of the kart fully to the right and mark the exterior wheel placement.
7. Draw two right triangles with the chalk using the drawn marks. Measure with an angle finder.
8. Repeat measurements for accuracy. Add angles together to find max rotation range.
DM - 30

## Slide 31: Steering Time Test 1 & 2
Overview: This test measures the steering system’s time response including time to achieve an angle, initiate a turn, and steering rate in both autonomous and manual modes in response to LiDAR commands, ensuring the system meets required safety response times.
Instructions:
1. Complete safety checklist. Secure the cart outside on level ground.
2. Perform tests by inputting commands.
3. Repeat all measurements for accuracy.
Results:
ER1- Manual Override Response Time: 150ms
ER2- Actuation Response Time: 850ms
ER3- Time to Achieve Angle: 310ms
ER4- Time to Start Turn: 250ms
ER5- Rate of Steering: 75
DM - 31

## Slide 32: Steering Specification Sheets
Customer Requirement | CR met? (Y or N) | Client Acceptable? (Y or N)
CR1 – Autonomous Steering | Y | Y
CR2 – Obstacle Detection/Avoidance | Y | Y
CR3 – User Control | Y | Y
CR4 – Safety | Y | Y
CR5 – Usability | Y | Y
Engineering Requirement | Target | Tolerance | Measured/Calculated Value | ER Met? (Y or N) | Client Acceptable (Y or N)
ER1- Manual Override Response Time | <500 ms | ±8.5ms | 150ms | Y | Y
ER2- Actuation Response Time | 45.5 ms | ±8.5ms | 850ms | Y | Y
ER3- Time to achieve angle | 500 ms | ±1s | 310ms | Y | Y
ER4- Time to start turn | 300 ms | ±1s | 250ms | Y | Y
ER5- Rate of steering | 100°/sec | ±1°/s | 75°/s | Y | Y
ER6- Steering Radius Left | 6m | ±0.025m | 4.143m | Y | Y
ER7- Steering Radius Right | 6m | ±0.025m | 4.721m | Y | Y
ER8- Max Rotation Range | 45° | ±5° | 44.7° | Y | Y
ER9 - Left Wheel Angle | 45° | ±5° | 42.83° | Y | Y
ER10 - Right Wheel Angle | 45° | ±5° | 48.91° | Y | Y
LQ - 32

## Slide 33: Throttle

## Slide 34: Throttle Functional Decomposition
34

## Slide 35: Throttle Concept Generation
Selection Criteria
  1.8Nm Minimum Useable Torque
  <500 ms Response Time
  Motor must control specific speeds
35

## Slide 36: Throttle Concept Selection
Specification Chart
Option Comparison
Morphological Matrix
Pugh Chart
Decision Matrix
36

## Slide 37: Throttle FMEA
37

## Slide 38: Throttle Initial Prototyping
Prototype 1 | Prototype 2 | Prototype 3
Question: How will the motor be mounted to pull on the throttle lever? Answer: Overhanging Motor Mount Takeaway: Interfered with pull-start and direct tension was too risky with surrounding parts of the motor. | Question: How will a cable interact with the stepper motor? Answer: Bowden Cable Takeaway: The placement of the Bowden cable body was causing added tension in the Bowden cable, which was poorly interacting with the spool on the stepper. | Question: How should the spool be designed to accurately pull the throttle lever? Answer: CNC Aluminum Spool Takeaway: The CNC process took longer than expected, but it resulted in a reliable spool to have the cable interact with the stepper motor.
38

## Slide 39: Throttle Final Design Summary
39

## Slide 40: Throttle Top Level Testing Summary
Experiment/Test | Relevant DRs | Testing Equipment Needed | Other Sources
Force Test | ER6 – Electric Pedal Force ER9 – Throttle Cable Force ER2 – Spring Force | Fish Scale Electrical Setup – Computer, Arduino, Wires, Battery, Driver Calipers Go-Kart | Jack Stands for Dry Test Outdoor Space Clear Weather Recording Sheet
Response Time Test | ER3 – Manual Override Response Time ER4 – Actuation Response Time | Electrical Setup – Computer, Arduino, Wires, Battery, Driver Timer Go-Kart | Cones Jack Stands for Dry Test Outdoor Space Clear Weather Recording Sheet Driver with Proper PPE
Speed Test | ER1 – Go-Kart Speed Range | Go-Kart Gasoline Electrical Setup – Computer, Arduino, Wires, Battery, Driver | Cones Jack Stands for Dry Test Outdoor Space Clear Weather Recording Sheet Driver with Proper PPE
Failsafe Test | ER5 – Failsafe Response Time | Killswitch Battery Timer Go-Kart | Driver with Proper PPE Outdoor Space Clear Weather Recording Sheet
Overall Stress Test | ER7 – Throttle Cable Velocity Er8 – Spool RPM to reach Maximum Throttle ER9 – Required Force to Pull Throttle Cable | Electrical Setup – Computer, Arduino, Wires, Battery, Driver Fish Scale Go-Kart | Jack Stands for Dry Test Outdoor Space Clear Weather Recording Sheet
40

## Slide 41: Throttle Force Test
Objective
Measure the forces of each subcomponent required to operate the throttle system
Requirements: forces in the throttle lever, electric pedal, and throttle cable are within safe and operational limits.
Equipment
Fish Scale
Go-Kart
Throttle Actuation Setup
Electric Pedal
Isolated Variables
Travel Distance of Electric Pedal
Travel Distance of Throttle Lever
Spring Force
Cold Engine
Results
Throttle Lever Force Range: 11.1 – 17.3 N
Electric Pedal Force Range: 44.4 – 53.3 N
Throttle Cable Force Range: 57.8 – 61.78 N
Throttle Lever Force Measurement
Electric Pedal Force Measurement
Throttle Cable Force Measurement
Steps
Secure the go-kart
Attach a fish scale to the throttle pedal and pull the pedal down to measure the electric pedal force
Attach the fish scale to the throttle cable near the spool or throttle lever and pull to measure throttle cable force
Measure the spring force of the throttle lever by attaching the fish scale and pulling
Repeat all measurements for accuracy
41

## Slide 42: Throttle Speed Test
Objective
Measure how fast the go-kart travels when a passenger uses the electric pedal to accelerate.
Requirements: the go-kart can reach up to 14 kph, and it has a functioning manual override.
Equipment
Go-Kar
Passenger with PPE
Chalk
Measuring Tape
Computer
Isolated Variables
Friction coefficient of the pavement
Weight of the go-kart
Distance go-kart will travel
Variables to Calculate
Go-Kart Speed using Frame-Rate Analysis
Steps
Power the go-kart and have the passenger press down on the brakes
Switch the mechanism from the autonomous control to the electric pedal control using the controls on the computer.
Mark 24-foot increments on pavement in a straight line.
Have the passenger press fully down on the throttle pedal while an individual records the area between two marked lines using a cellphone
Allow the rider to fully ride through two set points while recording on a cellphone.
Have the rider engage the failsafe and record results. Run more trials for better results and keep distance traveled constant.
Results
Speed Range During Dry Test: 3.4 – 10.69 m/s
Speed Range During Mechanical Control Test: 3.63 – 3.67 m/s ~ 13.14kph
Customer Requirement – up to 14 kph
42

## Slide 43: Throttle Actuation Response Time Test
Actuation Response Time
This test determines the amount of time required to reach maximum throttle using the actuation system at a set distance. This test also determines the spool’s RPM at maximum throttle.
Equipment
Go-Kart
Timer
Video Recording Device
Tape
Chalk
Isolated Variables
24ft. Set Traveling Distance
Failsafe Response Test
Spool RPM
Steps
Measure 24ft increments using a tape measurer and mark each increment using chalk.
Place the front tires of the go-kart behind the first chalk line.
Step away from the scene far enough to catch the kart and the second 24ft mark within the camera frame.
Begin recording and have a driver flash a signal right before the stepper is actuated. Record until the back tires pass the second chalk line.
Record results and repeat for accuracy.
Results:
Actuation Response Time: 100 ms
  Time From 100% Actuation to Full Throttle: 5.55 sec
Spool RPM: 15 RPM
Engineering Requirements:
Actuation Response Time of below 500 ms
Spool RPM between 10-20 rpm
Requirements: Fulfilled
43

## Slide 44: Throttle Response Time Test
Failsafe Response Time
This test measures how fast the throttle lever returns to the “zero throttle” position. This test fulfills the engineering requirements of having a failsafe response time below 500ms.
Equipment
Timer
Video Camera
Go-Kart
  Throttle Lever
  Stepper Motor
Isolated Variables
Actuation Response Time
Spool RPM
Steps
Turn the spool so that the stepper is calibrated and there is no slack in the line
From the calibrated position, turn the spool until the throttle lever reaches maximum throttle (i.e., the lever cannot be pulled farther out)
Begin recording using the video camera and timer, as the spool is released
Record results and repeat for accuracy
Results:
Failsafe Response Time: 0.12 seconds
Engineering Requirement:
Must be less than 500ms
Requirement: Fulfilled
44

## Slide 45: Throttle Specification Sheets
Throttle Customer Requirement Summary Table |  | 
Customer Requirement | CR met? (Y or N) | Client Acceptable? (Y or N)
CR1 – Autonomous Navigation | N | -
CR2 – User Control/Manual Override | Y | -
CR3 – State Monitoring/Diagnostics | N | -
CR4 – Performance | Y | -
CR5 – Safety | Y | -
CR6 – Usability | Y | -
Throttle Engineering Requirements Summary Table |  |  |  |  | 
Engineering Requirement | Target | Tolerance | Measured/ Calculated Value | ER met? (Y or N) | Client Acceptable? (Y or N)
ER1 – Maximum Speed | 1.34-3.85 m/s | ±0.5 m/s | 3.67 m/s | Y | Y
ER2 – Throttle Lever Force | 10-20 N | ±1 N | 11.1 – 17.3 N | Y | -
ER3 – Manual Override Response Time | <500 ms | ±10 ms | - | - | -
ER4 – Actuation Response Time | 37-54 ms | ±10 ms | - | - | -
ER5 – Failsafe Response Time | <500 ms | ±10 ms | - | - | -
ER6 – Electrical Pedal Force Range | 35-55 N | ±10 N | 44.4 – 53.3 N | Y | -
ER7 – Throttle Cable Velocity | 0.46-0.66 m/s | ±0.1 m/s | - | - | -
ER8 – Spool RPM at Maximum Throttle | 450 – 650 rpm | ±50 rpm | - | - | -
ER9 – Required Force to Pull Throttle Cable | 62 N | ±5 N | 57.8 – 61.78 N | Y | -
45

## Slide 46: Project Management

## Slide 47: Schedule
Brakes
  Fall 2025
  Spring 2026
Steering
  Fall 2025
  Spring 2026
Throttle
  Fall 2025
  Spring 2026
EC - 47

## Slide 48: Budget – General
EC - 48

## Slide 49: Bill of Materials – Mechanical Subteams
EC - 49

## Slide 50: Bill of Materials – Misc and Electrical
EC - 50

## Slide 51: Future Work
General
  Continued Testing
Brakes
  Improve force applied to rotor
  Real time motor calibration
Steering
  Improve steering radius
Throttle
  Enhance Acceleration Control
  Optimize Throttle Lever Sensor
AI Generated Photo of Autonomous NAU Buggy provided by Boeing
NP - 51

## Slide 52: Thank You! Questions?
Notes: 5 min for questions

## Slide 53: Appendix

## Slide 54: Brakes QFD

## Slide 55: Steering QFD

## Slide 56: Throttle QFD

## Slide 57: Brakes Gantt Schedules
Brakes Fall 2025 Gantt Schedule
Brakes Spring 2026 Gantt Schedule

## Slide 58: Steering Gantt Schedules
Steering Fall 2025 Gantt Schedule
Steering Spring 2026 Gantt Schedule

## Slide 59: Throttle Gantt Schedules
Throttle Fall 2025 Gantt Schedule
Throttle Spring 2026 Gantt Schedule

## Slide 60: Citations - Brakes
Brakes Literature Review
[1] D. Halliday and R. Resnick, Fundamentals of Physics, 10th ed. Hoboken, NJ: Wiley, 2013.
[2] J. D. Halderman, Automotive Brake Systems, 7th ed. Boston, MA: Pearson, 2019.
[3] M. Haataja and T. Leinonen, “On the distribution of braking forces in road braking,” SAE Technical Paper Series, Dec. 2000. doi:10.4271/2000-01-3413
[4] P. S. Bokare and A. K. Maurya, “Acceleration-deceleration behaviour of various vehicle types,” Transportation Research Procedia, vol. 25, pp. 4733–4749, 2017. doi:10.1016/j.trpro.2017.05.486
[5] S. G. Shadle, L. H. Emery, and H. K. Brewer, “Vehicle Braking, Stability and Control,” Login - CAS – central authentication service, https://www-jstor-org.libproxy.nau.edu/stable/44668097?seq=6 (accessed Sep. 14, 2025).

## Slide 61: Citations - Steering
Steering Literature Review
[6] B. Mok, M. Johns, S. Yang, and W. Ju, “Reinventing the Wheel,” Oct. 2017, doi: https://doi.org/10.1145/3126594.3126655.
[7] W. Kim, C. Kang, Y.-S. Son, and C. Chung, “Nonlinear Steering Wheel Angle Control Using Self-Aligning Torque with Torque and Angle Sensors for Electrical Power Steering of Lateral Control System in Autonomous Vehicles,” Sensors, vol. 18, no. 12, p. 4384, Dec. 2018, doi: https://doi.org/10.3390/s18124384.
[8] J. E. Naranjo, C. González, R. García, and T. de Pedro, “Electric Power Steering Automation for Autonomous Driving,” Lecture Notes in Computer Science, pp. 519–524, 2005, doi:https://doi.org/10.1007/11556985_67.
[9] P. Falcone, F. Borrelli, J. Asgari, H. E. Tseng, and D. Hrovat, “Predictive Active Steering Control for Autonomous Vehicle Systems,” IEEE Transactions on Control Systems Technology, vol. 15, no. 3, pp. 566–580, May 2007, doi: https://doi.org/10.1109/tcst.2007.894653.
[10] M. K. Mishra, A. Maurya, and R. R. Dev, “Automatic Steering System,” International Journal of Science and Research (IJSR), vol. 5, no. 5, pp. 105–107, May 2016, doi:10.21275/NOV163265

## Slide 62: Citations - Throttle
Throttle Literature Review – Used in the Doc
[11] T. Stolte, Gerrit Bagschik, and M. Maurer, “Safety goals and functional safety requirements for actuation systems of automated vehicles,” Nov. 2016, doi: https://doi.org/10.1109/itsc.2016.7795910.
[12] J. F. Arango et al., “Drive-By-Wire Development Process Based on ROS for an Autonomous Electric Vehicle,” Sensors, vol. 20, no. 21, p. 6121, Oct. 2020, doi: https://doi.org/10.3390/s20216121.
[13] ﻿"NHTSA Rulemakings Related to Automated Driving System-Equipped Vehicles NHTSA Rulemakings Related to Automated Driving System- Equipped Vehicles," 2024. Available: https://www.nhtsa.gov/sites/nhtsa.gov/files/2024-05/Report-to-Congress-NHTSA-Rulemakings-Related-to-Automated-Driving-System-Equipped-Vehicles.pdf
[14] R. Conatser, J. Wagner, S. Ganta, and I. Walker, “Diagnosis of automotive electronic throttle control systems,”Control Engineering Practice, vol. 12, no. 1, pp. 23–30, Jan. 2004, doi: https://doi.org/10.1016/s0967-0661(02)00281-2.
[15] S. Xu, H. Peng, Z. Song, K. Chen, and Y. Tang, “Accurate and Smooth Speed Control for an Autonomous Vehicle,” IEEE Xplore, Jun. 01, 2018. https://ieeexplore.ieee.org/document/8500519 (accessed Mar. 19, 2023).
﻿Throttle Literature Review – Used in the Semester
[1] H. Luo, X. Hu, and L. Huang, "A Hybrid Model for Vehicle Acceleration Prediction," Sensors (Basel, Switzerland), vol. 23, no. 16, p. 7253, 2023
﻿[2] A. Altby and D. Majdandzic, "Design and implementation of a fault-tolerant drive-by-wire system.” Accessed: Nov. 26, 2025.
﻿[3] H. Mauser, E. Thurner, and E. Hw, "Electronic Throttle Control -A Dependability Case Study.” Accessed: Nov. 26, 2025.
﻿[4] H. Guo, D. Cao, H. Chen, Z. Sun, and Y. Hu, "Model predictive path following control for autonomous cars considering a measurable disturbance: Implementation, testing, and verification," Mechanical Systems and Signal Processing, vol. 118, pp. 41-60, Mar. 2019
﻿[5] S. Xu, H. Peng, Z. Song, K. Chen, and Y. Tang, "Accurate and Smooth Speed Control for an Autonomous Vehicle," IEEE Xplore, Jun. 01, 2018.
[6] N. Kolekar and S. Shelar, "Certified Organization) Website: www," International Journal of Innovative Research in Science, Engineering and Technology (An ISO, vol. 3297, 2007,
﻿[7] ﻿R. Conatser, J. Wagner, S. Ganta, and I. Walker, "Diagnosis of automotive electronic throttle control systems," Control Engineering Practice, vol. 12, no. 1, pp. 23-30, Jan. 2004,
﻿[8] ﻿"Drive-by-wire Conversion for Autonomous Vehicle," Robotics Knowledgebase, Dec. 07, 2022.
[9] ﻿"Digital Twin System for Automotive Safety with Integration of a Safety Controller," Research portal Eindhoven University of Technology, 2024.
﻿[10] ﻿V. S. Dubey, Ruhshad Kasad, and K. Agrawal, "Autonomous Braking and Throttle System: A Deep Reinforcement Learning Approach for Naturalistic Driving" arXiv (Cornell University), Jan.2021
[11] R. Nalbandian, T. Blais, and R. Horth, "A Recommended New Approach on Motorization Ratio Calculations of Stepper Motors." Accessed: Oct. 16, 2025. [Online]. Available: https://ntrs.nasa.gov/api/citations/20150004072/downloads/20150004072.pdf
[12] S. Thapa, "3D Printing of Automobile Power Transmission System Using Tough PLA," Urn.fi, 2020, doi: https://www.theseus.fi/handle/10024/343865.
[13] M. Venczel, Á. Veress, and Z. Peredy, "Past and Future Practical Solutions for Torsional Vibration Damping in Vehicle Industry," Periodica Polytechnica Transportation Engineering, vol. 50, no. 4, pp. 318-329, Aug. 2022, doi: https://doi.org/10.3311/PPtr.19194.
[14] Mattikalli, S., Rayar, V., Yallure, B., Akki, S., & Thane, S. (2024). AUTOSAR-enabled throttle position sensor testing and analysis using MATLAB. 2024 IEEE North Karnataka Subsection Flagship International Conference (NKCon), 1-5. https://doi.org/10.1109/nkcon62728.2024.10775293
[15] H. Niaz, Muhammad Abdullah Sheeraz, and M. A. Naeem, "Multi-Parametric Analysis of a Mimicked Accelerating Pedal (Via DC Motor) of an Electric Vehicle," DOAJ (DOAJ: Directory of Open Access Journals), pp. 48-48, Oct. 2023, doi: https://doi.org/10.3390/asec2023-15253.
[16] ﻿Oluwatobiloba Adejumo, "Safety of 3D Printing in Automotive Industries," SSRN Electronic Journal, Jan. 2025, doi: https://doi.org/10.2139/ssrn.5112375.
[17] ﻿J. Lee, K. Oh, and K. Yi, "DEVELOPMENT OF AN EMERGENCY CONTROL ALGORITHM FOR A FAIL-SAFE SYSTEM IN AUTOMATED DRIVING VEHICLES." Available: https://www-esv.nhtsa.dot.gov/Proceedings/26/26ESV-000101.pdf
[18] ﻿Arduino, "Power Consumption on Arduino Boards," Arduino.cc, 2024. https://docs.arduino.cc/learn/electronics/power-consumption/
[19] "NHTSA Rulemakings Related to Automated Driving System-Equipped Vehicles NHTSA Rulemakings Related to Automated Driving System- Equipped Vehicles," 2024. Available: https://www.nhtsa.gov/sites/nhtsa.gov/files/2024-05/Report-to-Congress-NHTSA-Rulemakings- Related-to-Automated-Driving-System-Equipped-Vehicles.pdf
[20]﻿Krystian Radlak, M. Szczepankiewicz, T. Jones, and P. Serwa, "Organization of machine learning based product development as per ISO 26262 and ISO/PAS 21448," arXiv (Cornell University), pp. 110-119, Dec. 2020, doi: https://doi.org/10.1109/prdc50213.2020.00022.

## Slide 63: Additional Citations
[16] Budynas, Shigley’s Mechanical Engineering Design, 11Th Edition, Si Units. S.L.: Mcgraw-Hill Education (As, 2020.)
[17]

## Slide 64: Other Engineering Calculations - Brakes
Maximum autonomous speed ( ) = 2.2352 m/s
Brake efficiency () = .7
Acceleration due to Gravity () = 9.81
Reaction time of vehicle () = 0.5 s
Acceleration of vehicle () = 6.87
Time to bring vehicle to complete stop ()
Distance traveled while stopping ()
Time to bring vehicle to complete stop () = 0.826 s
Distance traveled while stopping () = 2.21 m
Notes: 1.5min max

## Slide 65: Other Engineering Calculations - Steering
Minimum Thickness for Motor Mount Plate
Minimum Thickness for U-Bracket

## Slide 66: Other Engineering Calculations - Throttle
F_throttle_min = 4.55;
theta_stepper = 90;
theta_lever = 22.7;
d_cable_min = 15;
d_wire = 1.5;
d_spool = 33.5;
friction_coeff = 0.16;
sigma_ult = 1800;
r_spool = d_spool/2;
rad_stepper = deg2rad(theta_stepper);
rad_lever = deg2rad(theta_lever);
% Spool Rotation Angle
theta_cable_bend = d_cable_min/r_spool;
Area_inner_wire = (pi*(d_wire)^2)/4;
% Calculate the output force
F_in = F_throttle_min * exp(friction_coeff*theta_cable_bend);
% Cable stress using the area of the inner wire
cable_stress = F_in / Area_inner_wire;
% Calculate the actual tensile force
F_ult = sigma_ult * Area_inner_wire;
% Calculate the Factor of Safety
FoS = F_ult / F_in; % Factor of Safety calculation
% Calculate Efficiency
n = F_throttle_min/F_in;
Assumptions | Values | Units
Horsepower of Go-Kart | 5.30 | Hp
Max Torque of Go-Kart at 2500rpm | 11.00 | Nm
Radius of Coupler (rCoupler) | 32 | mm
Maximum Tensile Strength of Coupler Screws ( σucs, max) | 175 | ksi
Stepper Motor Holding Torque (TMotor, max) | 2.4 | Nm
Measurements | Values | Units
Lever Force to 100% Throttle (FThrottle, min) | 4.55 | N
Max turn of Stepper (θStepper) | 90 | degrees
Angle of throttle lever turn (θLever) | 22.7 | degrees
Cable Distance to Full Throttle (dCable, min) | 15 | mm
Diameter of Spool (dspool) | 33.5 | mm
Friction Coefficient in Cable (μ) [1] | 0.16 | 
Ultimate Cable Stress (σult) [3] | 1800 | MPa
Table 1: Assumptions
Bowden Cable Analysis
Table 2: Measurements