## Slide 1: Final Testing Results Boeing Autonomous
Elise C., Selina C., Jake K., Marek L., Desirae M., Natasa P., Lily Q.

## Slide 2: Design Requirements Summary

## Slide 3: All Systems
CR # | Customer Requirement | Description
CR1 | Autonomous Navigation | The buggy must steer, accelerate, and brake on a predefined path without any human interference.
CR2 | Obstacle Detection | The buggy must be able to detect static and dynamic obstacles in its path to stop before collisions.
CR3 | Manual Override | Each autonomous sub-team must have a manual mode that allows the driver to mechanically control the buggy, full disengaging the autonomous mode to avoid system interference.
CR4 | Real-Time State Monitoring | The buggy must provide real-time feedback to a computer-based monitoring system that can determine errors and provide live-time data that can be monitored during travel time.
CR5 | Emergency Stop Mechanism | There must be a physical emergency stop button that safely halts the vehicle mounted in an accessible area of the go-kart.
CR6 | Fail-Safe Design | The system must be able to disengage all electrical components and stop safely in the event of any failure.
CR7 | Battery Life for Continuous Operation | The buggy must operate autonomously for a minimum of 20 minutes on a single battery charge.
CR8 | Support for Driver Assistance and Autonomous Modes | The system must support both manual and autonomous modes during every drive or operation.
CR9 | Actuator Control for Subfunctions | The system must enable lane-keeping assist and other driver aids by controlling the buggy’s main subfunctions.
CR10 | Integration with Open-Source Autonomous Platforms | The system must integrate with open-source self-driving software and sensor data to enable autonomous driving capabilities.
CR11 | Prioritized Safety Features | The system must prioritize safety features like emergency stop, kill switch, and validated fail-safe mechanisms.
CR12 | Closed-Course Testing with Controlled Parameters | The system must be tested on a closed course with defined performance parameters (e.g., speed, path accuracy, obstacle avoidance) to validate its functionality and reliability.
CR13 | Comprehensive Documentation and Handover | The project must deliver a complete handover package within a comprehensive report including an operations manual, CAD models, Bill of Materials (BOM), software integration details, test reports, and a prototype demonstration of how to use the self-driving features.
3
Engineering Requirements
The system's obstacle detection and avoidance algorithms shall have a response time of less than 500 ms to ensure safe operation.
The buggy's top autonomous speed shall be no more than 14 kph.
The system shall operate for a minimum of 20 minutes on a single battery charge during continuous autonomous operation.

## Slide 4: Top Level Testing Summary

## Slide 5: Steering
Experiment/Test | Relevant DRs | Testing Equipment Needed | Other Sources
Motor Controlled Steering Test | ER6- Left turn radius ER7- Right turn radius | Means to make a video Measuring tape Go Kart | Clear weather Clear course in parking lot Test driver
Time Test 1 (Steering Dynamics) | ER3- Time to Achieve Angle ER4- Time to Start Turn ER5- Rate of Steering | Means to make a video Measuring tape Stopwatch Go Kart | Clear weather Clear course in parking lot No oil/water on roads
Time Test 2 (Override and Safety Response) | ER1- Manual Override Response ER2- Actuation Response Time | Means to make a video Stopwatch Go Kart | Clear weather Clear course in parking lot No oil/water on roads
Steering Rotation Test | ER8- Max Rotation Range ER9 - Left Wheel Angle ER10 - Right Wheel Angle | Measuring tape Go Kart Means to make a video Means to mark rotation | Clear weather Clear course in parking lot Time
LQ 6

## Slide 6: Throttle
EC 7
Experiment/Test | Relevant DRs | Testing Equipment Needed | Other Sources
Force Test | ER6 – Electric Pedal Force ER9 – Throttle Cable Force ER2 – Spring Force | Fish Scale Electrical Setup – Computer, Arduino, Wires, Battery, Driver Calipers Go-Kart | Jack Stands for Dry Test Outdoor Space Clear Weather Recording Sheet
Response Time Test | ER3 – Manual Override Response Time ER4 – Actuation Response Time | Electrical Setup – Computer, Arduino, Wires, Battery, Driver Timer Go-Kart | Cones Jack Stands for Dry Test Outdoor Space Clear Weather Recording Sheet Driver with Proper PPE
Speed Test | ER1 – Go-Kart Speed Range | Go-Kart Gasoline Electrical Setup – Computer, Arduino, Wires, Battery, Driver | Cones Jack Stands for Dry Test Outdoor Space Clear Weather Recording Sheet Driver with Proper PPE
Failsafe Test | ER5 – Failsafe Response Time | Killswitch Battery Timer Go-Kart | Driver with Proper PPE Outdoor Space Clear Weather Recording Sheet
Overall Stress Test | ER7 – Throttle Cable Velocity ER8 – Spool RPM to reach Maximum Throttle ER9 – Required Force to Pull Throttle Cable | Electrical Setup – Computer, Arduino, Wires, Battery, Driver Fish Scale Go-Kart | Jack Stands for Dry Test Outdoor Space Clear Weather Recording Sheet

## Slide 7: Detailed Testing Plans

## Slide 8: Steering – Time Test 1
SC 8
This test measures the time response to achieve an angle, to start a turn, and the rate of steering. These values will allow for the proper preparation of response time from the system to meet safety requirements.
Equipment | Variables Isolated for measurement | Variables to be Calculated from Results
Camera Measuring tape Phone timer Space to turn wheels | Time to achieve an angle Time to start a turn Rate of steering (Time to perform a turn) | N/A
Complete safety checklist. Secure the cart on level ground. | 2. Preform test from computer and record results. | 3. Use video to determine values for each action. Repeat all measurements for accuracy.

## Slide 9: Steering – Time Test 1 Demo
SC 9
ER3- Time to Achieve Angle: 310ms
ER4- Time to Start Turn: 250ms
ER5- Rate of Steering: 75

## Slide 10: Steering – Time Test 2
DM 17
This test measures the time the steering autonomous and manual modes take to respond to the LiDAR commands. These values are important for ensuring that the system can respond in the time required to be deemed safe.
Equipment | Variables Isolated for measurement | Variables to be Calculated from Results
Camera Phone timer Empty parking lot | Manual override response time Actuation response time | N/A
Complete safety checklist. Secure the cart on level ground. | 2. Preform test from computer and record results. | 3. Use video and timer to determine values for each action. Repeat all measurements for accuracy.

## Slide 11: Steering – Time Test 2 Demo
DM 18
ER1- Manual Override Response Time: 150ms

## Slide 12: Steering – Time Test 2 Demo
DM 18
ER2- Actuation Response Time: 850ms
*First successful test of steering wheel being moved autonomously! *

## Slide 13: Throttle Previous Tests
Force Test
Measures the forces of each subcomponent required to operate the throttle system.
This test fulfills the following requirements: the forces used to control the throttle lever, the electric pedal, and the throttle cable force are within the required safe and operational limits.
Results:
Throttle Lever Force Range: 11.1 – 17.3 N (safe range)
Electric Pedal Force Range: 44.4 – 53.3 N (safe range)
Throttle Cable Force Range: 57.8 – 61.78 N (safe range)
Design Requirements: Fulfilled
Throttle Lever Force Measurement
Electric Pedal Force Measurement
Throttle Cable Force Measurement
Speed Test
This test answers how fast the go-kart travels when a passenger uses the electric pedal to accelerate.
This test fulfills the following customer requirements: the go-kart can reach up to 14 kph, and the go-kart has a functioning manual override.
Results
Speed Range During Dry Test:
3.4 – 10.69 m/s
Speed Range During Mechanical Control Test:
3.63 – 3.67 m/s ~ 13.14kph
Customer Requirement: up to 14 kph
Design Requirement: Fulfilled
NP 12

## Slide 14: Throttle Test 3
Actuation Response Time
  This test determines the amount of time required to reach maximum throttle using the actuation system at a set distance. This test also determines the spool’s RPM at maximum throttle.
Equipment | Variables Isolated for measurement | Variables to be Calculated from Results
Go-Kart Timer Video Recording Device Tape Measurer Chalk | 24 ft set Traveling Distance Failsafe Response Time Spool RPM | N/A
Steps |  |  |  | 
Measure 24ft increments using a tape measurer and mark each increment using chalk. | Place the front tires of the go-kart behind the first chalk line. | Step away from the scene far enough to catch the kart and the second 24ft mark within the camera frame. | Begin recording and have a driver flash a signal right before the stepper is actuated. Record until the back tires pass the second chalk line. | Record results and repeat for accuracy.
NP 13

## Slide 15: Throttle Test 3 Demo
Results:
Actuation Response Time: 100 ms
  Time From 100% Actuation to Full Throttle: 5.55 sec
Spool RPM: 15 RPM
Engineering Requirements:
Actuation Response Time of below 500 ms
Spool RPM between 10-20 rpm
Requirements: Fulfilled
NP 14

## Slide 16: Throttle Test 4
Failsafe Response Time
  This test measures how fast the throttle lever returns to the “zero throttle” position. This test fulfills the engineering requirements of having a failsafe response time below 500ms.
Equipment | Variables Isolated for measurement | Variables to be Calculated from Results
Timer Video Camera Go-Kart Throttle Lever Stepper Motor | Actuation Response Time Spool RPM | N/A
Steps |  |  | 
Turn the spool so that the stepper is calibrated and there is no slack in the line. | From the calibrated position, turn the spool until the throttle lever reaches maximum throttle (i.e., the lever cannot be pulled farther out) | Begin recording using the video camera and timer, as the spool is released. | Record results and repeat for accuracy.
EC 15

## Slide 17: Throttle Test 4 Demo
Results:
Failsafe Response Time: 0.12 seconds
Engineering Requirement:
Must be less than 500ms
Requirement: Fulfilled
EC 16

## Slide 18: Specification Sheet Preparation

## Slide 19: Steering
Customer Requirement | CR met? (Y or N) | Client Acceptable? (Y or N)
CR1 – Autonomous Steering | Y | -
CR2 – Obstacle Detection/Avoidance | Y | -
CR3 – User Control | Y | -
CR4 – Safety | Y | Y
CR5 – Usability | Y | Y
LQ 25
Engineering Requirement | Target | Tolerance | Measured/Calculated Value | ER Met? (Y or N) | Client Acceptable (Y or N)
ER1- Manual Override Response Time | <500 ms | ±8.5ms | 150ms | Y | -
ER2- Actuation Response Time | 45.5 ms | ±8.5ms | 850ms | Y | -
ER3- Time to achieve angle | 500 ms | ±1s | 310ms | Y | -
ER4- Time to start turn | 300 ms | ±1s | 250ms | Y | -
ER5- Rate of steering | 100°/sec | ±1°/s | 75°/s | Y | -
ER6- Steering Radius Left | 6m | ±0.025m | 4.143m | Y | Y
ER7- Steering Radius Right | 6m | ±0.025m | 4.721m | Y | Y
ER8- Max Rotation Range | 45° | ±5° | 44.7° | Y | Y
ER9 - Left Wheel Angle | 45° | ±5° | 42.83° | Y | Y
ER10 - Right Wheel Angle | 45° | ±5° | 48.91° | Y | Y

## Slide 20: Throttle
NP 19
Throttle Customer Requirement Summary Table |  | 
Customer Requirement | CR met? (Y or N) | Client Acceptable? (Y or N)
CR1 – Autonomous Navigation | Y | -
CR2 – User Control/Manual Override | Y | Y
CR3 – State Monitoring/Diagnostics | Y | -
CR4 – Performance | Y | Y
CR5 – Safety | Y | Y
CR6 – Usability | Y | Y
Throttle Engineering Requirements Summary Table |  |  |  |  | 
Engineering Requirement | Target | Tolerance | Measured/ Calculated Value | ER met? (Y or N) | Client Acceptable? (Y or N)
ER1 – Maximum Speed | 1.34-3.85 m/s | ±0.5 m/s | 3.67 m/s | Y | Y
ER2 – Throttle Lever Force | 10-20 N | ±1 N | 11.1 – 17.3 N | Y | Y
ER3 – Manual Override Response Time | <500 ms | +25 ms -5 ms | 50ms | Y | -
ER4 – Actuation Response Time | 90-150 ms | ±10 ms | 100ms | Y | -
ER5 – Failsafe Response Time | <500 ms | ±10 ms | 120ms | Y | Y
ER6 – Electrical Pedal Force Range | 35-55 N | ±10 N | 44.4 N | Y | Y
ER7 – Throttle Cable Velocity | 0.02-0.05m/s | ±0.025 m/s | 0.03m/s | Y | -
ER8 – Spool RPM at Maximum Throttle | 10-20 rpm | ±5 rpm | 15 rpm | Y | -
ER9 – Required Force to Pull Throttle Cable | 62 N | ±5 N | 57.8 N | Y | Y

## Slide 21: QFD

## Slide 22: Steering
LQ 29

## Slide 23: Throttle
Copyright © 2005 Kevin Otto
Please freely distribute and modify, but properly reference and maintain this contact information in the sheet.
www.robuststrategy.com
kevin_n_otto@yahoo.com
http://www.kevinotto.com/RSS/templates/QFD Template.xls
Modified from a template from Design4X Inc.
EC 22

## Slide 24: Thank you!
Any Questions?

## Slide 25: Brakes
Experiment/Test | Relevant DRs | Testing Equipment Needed | Other Resources
Motor Test | ER 2 - Actuation Response Time ER 3 - Brake Disengage Time ER 6 - Speed of Actuation | Camera Capable of Slow-Motion Recording Stopwatch Battery Motor PPE Brake Caliper | Personal protective equipment in addition to at least one EE and one EE are required.
Static Brake Test | ER 4 - Time to Brake Kart from Maximum Speed ER 13 - Maintainability of Components | Camera Capable of Slow-Motion Recording Stopwatch Battery Motor PPE Brake Caliper | Personal protective equipment in addition to at least one EE and one EE are required.
Brake Stress Test | ER 1 - Manual Override Response Time ER 7 - Maintaining User Control ER 12 - Intuitive Brake Failsafe | Go-kart Assembled subsystem PPE Battery Failsafe Mounted | Personal protective equipment in addition to at least one EE and one EE are required.
System Limit Test | ER 10 - Number of Brake Cycles from Full Battery ER 11 - 20 Minute Operation Time | Go-kart Assembled subsystem PPE Battery Failsafe Mounted | Personal protective equipment in addition to at least one EE and one EE are required.
Dynamic Brake Test | ER 5 - Distance Traveled while Braking ER 8 - Speed of brake in rainy conditions* ER 9 - Speed of brake in snowy conditions* | Go-kart Assembled subsystem PPE Battery Failsafe Mounted | To properly test ER 8 and 9 we would need the proper weather conditions.
5

## Slide 26: Brakes
JK 24
Customer Requirement | CR met? (Y or N) | Client Acceptable? (Y or N)
CR1 – Autnomous Navigation | N | -
CR2 – Obstacle Detection/Avoidance | N | -
CR3 – Manuel Override | Y | -
CR4 – Fail-Safe Design | Y | -
CR5 – Usability | Y | -
Engineering Requirement | Target | Tolerance | Measured / Calculated Value | ER met? (✓ or X) | Client Acceptable (✓ or X)
ER1 - Manual Override Response Time | ≤ 500 ms | ±50 ms | 0.25 s (250 ms) | ✓ | ✓
ER2 - Actuation Response Time | ≤ 500 ms | ±50 ms | 72 ms (full 120° actuation) | ✓ | ✓
ER3 - Brake Disengage Time | ≤ 500 ms | ±50 ms | TBD (actuation disengage = 87 ms from data) | ✓ | ✓
ER4 - Brake Disengage Time (dynamic) | ≤ 1.5 s | ±0.3 s | TBD (very short - supported by 14.4× FoS) | TBD | TBD
ER5 - Distance Traveled During Braking (dry) | ≤ 6 m | ±1 m | 0.55 m (peak torque) / 1.28 m (continuous torque) | ✓ | ✓
ER6 - Speed of Actuation | TBD | TBD | 120° in 72 ms (≈1.67°/ms) | ✓ | ✓
ER7 - Ability to maintain user control | Full manual control retained | N/A | User maintains control | ✓ | ✓
ER8 - Braking in Rainy Conditions | Distance increase <50–150% vs dry | Qualitative/TBD | TBD | TBD | TBD
ER9 - Braking in Snowy Conditions | Distance increase <100–200% vs dry | Qualitative/TBD | TBD | TBD | TBD
ER10 - Number of times kart can brake before failure | ≥ 1000 cycles | ±100 cycles | TBD | TBD | TBD
ER11 - Operation Time (continuous) | ≥ 20 min | TBD | TBD | TBD | TBD
ER12 - Intuitive Failsafe Testing | ≥ 90% third-party success | Qualitative | TBD | TBD | TBD
ER13 - Maintainability of Components | Service < 30 min | Qualitative | TBD | TBD | TBD
ER14 - Protection of Subsystem | Weatherproof | Qualitative | TBD | TBD | TBD
ER-Torque Contribution (from caliper tests) | Sufficient to support ER4/ER5 | Qualitative | 4,628 N clamping force (FoS 14.4) | ✓ | ✓

## Slide 27: Brakes
28

## Slide 28: Brakes – Motor Test
9
The purpose of this test is to find the time needed to move the motor once given a command, the speed needed to actuate across the needed range of motion, and the time needed to move back from the full state of motion
Equipment | Variables Isolated for measurement | Variables to be Calculated from Results
Camera Capable of Slow-Motion Recording Stopwatch Battery Motor PPE Brake Caliper | Time needed for motor response Time needed for motor to finish engaging the brake Time needed for motor to de-engage the brake | N/A
Complete safety checklist. Secure the cart | 2. Begin recording the system with camera | 3. Provide commands for motor to actuate both directions fully | 4. Measure time for each variable | 5. Repeat across three trials to gather an average | 6. Process data from recording and analyze data for ER specifications

## Slide 29: Brakes Motor Test Demo
10

## Slide 30: Brakes – Static Brake Test
11
The purpose of this test is to find the time once actuation begins needed to stop the brake given a starting speed equal to or larger than our maximum speed.
Equipment | Variables Isolated for measurement | Variables to be Calculated from Results
Camera Capable of Slow-Motion Recording Stopwatch Battery Assembled Sub-System PPE | Time for one rotation of the tire Time from start of actuation to when the wheel is stopped completely | Speed of Wheel Estimated Distance Traveled (Estimating Dynamic Test Results)
Complete safety checklist. Secure the cart | 2. Mark a spot on the tire, begin recording and spinning the tire | 3. Provide commands for motor to actuate until at maximum range | 4. Measure speed of tire and time required to stop the tire from beginning of actuation | 5. Repeat across three trials to gather an average | 6. Process data from recording and analyze data for ER specifications

## Slide 31: Brakes – Static Brake Test Demo
12

## Slide 32: Brakes – Stress Test
9
The purpose of this test is to find the number of cycles the system can run until failure while dual testing for our 20-minute operation time customer requirement.
Equipment | Variables Isolated for measurement | Variables to be Calculated from Results
Battery Motor PPE Brake Caliper Stopwatch | Cycles per 20-minute operation Time before failure (max 20 minutes) | N/A
Complete safety checklist. Secure the cart | 2. Begin the program that repeats cycles and counts each cycle | 3. Finish the 20-minute test | 4. Check manufactured parts for failure | 5. Process data from recording and analyze data for ER/CR specifications

## Slide 33: Brakes – Stress Test
12

## Slide 34: Brakes – Failsafe Test
9
The purpose of this test is to find how effective the sensor-based failsafe the team installed is. In addition, this will allow the sub-team to test the durability of the manufactured parts.
Equipment | Variables Isolated for measurement | Variables to be Calculated from Results
Battery Motor PPE Limit Switch | Response Speed | N/A
Complete safety checklist. Secure the cart | 2. Engage the autonomous brake. | 3. Push the manual brake pedal, activating the limit switch. | 4. Record Results | 5. Process data from recording and analyze data for ER/CR specifications

## Slide 35: Brakes – Failsafe Test
12

## Slide 36: Brakes – Dynamic Brake Test
9
The purpose of this test is to find the time needed to stop from maximum throttle and the distance traveled from the start of actuation.
Equipment | Variables Isolated for measurement | Variables to be Calculated from Results
Battery Motor PPE Brake Caliper Stopwatch Chalk | Distance Traveled Time needed to reach 0mph | Brake efficiency
Complete safety checklist. Secure the cart | 2. Make chalk lines every 22 feet and place kart down perpendicular to the lines | 3. Reach maximum throttle speed and autonomously brake the kart. | 4. Record the test and distance once braking starts. | 5. Process data from recording and analyze data for ER/CR specifications

## Slide 37: Brakes – Dynamic Brake Test Demo
12